## Slide 1
Mayank Parasar, Natalie Enright Jerger, Paul V. Gratz, Joshua San Miguel and Tushar Krishna
SWAP: Synchronized Weaving of Adjacent Packets for Network Deadlock Resolution
mparasar3@gatech.edu
http://synergy.ece.gatech.edu

## Slide 2: Challenge: Routing Deadlock
9
5
10
6
5
9
6
10
Deadlock
5
Destination Router-5
Network
Network
Network
Network
Deadlock: Cyclic dependence between packets
Renders the forward progress of packets impossible
Correctness problem, can cause system failure

## Slide 3: Channel Dependency Graph (CDG)
F
A
B
E
D
C
Cycle
Function of Topology and Routing Algorithm
Deadlock occurs because of cycles present in the channel dependency graph of the topology

## Slide 4
Design | Resolution Type | Full Path Diversity | No Extra VCs | Topology Agnostic | No Deadlock Detection
Dally/Turn Restriction [1] | No Cycle |  |  |  | 
Duato/Escape VC [2] | Escape |  |  |  | 
Injection Restriction [3] | Bubble |  |  |  | 
Deflection [4] | Misroute |  |  |  | 
Coordination [5] | Synchronize |  |  |  | 
? | ?? |  |  |  | 
*in all VCs except escape VC
*
Qualitative Comparison of Deadlock Freedom Mechanisms
*
Can we do better?
[1]:
[2]:
[3]:
[4]:
[5]:
Deadlock-free message routing in multiprocessor interconnection networks [IEEE Trans. Computer, 1987]
A new theory of deadlock-free adaptive routing in wormhole networks. [IEEE Trans. On Parallel and Dist. Sys, 1993]
Bubble Flow Control [IPDPS 2011]
BLESS [ISCA’09] CHIPPER [HPCA’11]
DISHA [IPDPS’95] Static Bubble [HPCA’17] SPIN [ISCA’18]

## Slide 5: Outline
Background: Deadlocks
Current Solutions
SWAP
  Walk-through
  Concept
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 6: Traffic Deadlock
Deadlock

## Slide 7: Swap to resolve traffic deadlock
Deadlock

## Slide 8: Key Terms
‘swapFwd’ packet always makes forward progress
‘swapBack’ packet is interchanged with swapFwd packet in SWAP
‘Backtrack’ is an act where ‘swapBack’ yield its buffer for ‘swapFwd’ to make forward progress

## Slide 9: SWAP to resolve Network Deadlock
9
5
10
6
5
9
6
10
Deadlock
Network
Network
Network
Network
SWAP
swapFwd
swapBack
backtrack
Eject
Deadlock Resolved!

## Slide 10: SWAP in network
A
B
C
F
E
D
Runtime Channel Dependency Graph
AB
BC
CD
DE
EF
FA
d
f
c
z
x
y
Cyclic
backtrack
c
backtrack
Acyclic
Eject
Deadlock Resolved

## Slide 11: SWAP: Key Idea
Swap implies interchanging two packets from two adjacent routers
Requires no additional buffers
Leverages the bidirectional links to simultaneously send two packets
Topology and Routing Algorithm agnostic
If any VC at the downstream is empty, swap is not performed

## Slide 12: Outline
Background: Deadlocks
Current Solutions
SWAP
  Walk-through
  Concept
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 13: SWAP Datapath - Concept
Periodic in-place exchange of packets can be used to break deadlock
Swap=0
Swap=0
clk
A
B
0
1
0
1
Router
Buffer
Packet
Swap=1
Swap=1
clk
A
B
1
0
1
0
Swap=0
Swap=0
clk
B
A
0
1
0
1

## Slide 14: SWAP Control Path
When to initiate a swap?
  Every router gets the chance to initiate a swap every p cycles
    p is configurable
  No explicit deadlock detection
How to swap?
  The router selects a packet and sends a swap_req to the downstream router at its output port
  If packet at any VC at the downstream is ejecting, swap is not performed

## Slide 15: Outline
Background: Deadlocks
Current Solutions
SWAP
  Walk-through
  Concept
  Router microarch
  Deadlock freedom proof
Evaluations
  Methodology
  Results
Conclusion

## Slide 16: Router Micro-Architecture
30% lower area than Escape VC router
4% higher area than XY/West-First router
Least expensive!

## Slide 17: SWAP Datapath - Router Microarchitecture
swapFwd
swapBack

## Slide 18: Outline
Background: Deadlocks
Current Solutions
SWAP
  Walk-through
  Concept
  Router microarch
  Deadlock freedom proof
Evaluations
  Methodology
  Results
Conclusion

## Slide 19: SWAP: Deadlock Freedom Proof
Deadlock-Freedom
  Every packet gets a chance to perform a swap, the network is deadlock free (i.e., no packed is blocked indefinitely)
  Enforced via round-robin priority for all router input ports
Livelock Freedom
  Backtracked packet can move forward by two hops before being backtracked again
  Enforced by period between swaps and fair VC selection scheme

## Slide 20: Outline
Background: Deadlocks
Current Solutions
SWAP
  Concept
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 21: Evaluations
Gem5 for full system and SE mode simulations
X86 and RISC-V ISA
Garnet2.0 for network simulation
SWAP uses random routing algorithm
SWAP uses VCT flow control
Evaluated on regular and irregular topologies
Evaluated on synthetic traffic patterns

## Slide 22: Outline
Background: Deadlocks
Current Solutions
SWAP
  Concept
  Definition
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion

## Slide 23: Synthetic Traffic
Chart: Uniform Random
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36
XY | 15.5562 | 15.5826 | 15.6326 | 15.6985 | 15.7761 | 15.8335 | 15.9328 | 16.0406 | 16.173 | 16.343 | 16.5357 | 16.7934 | 17.1285 | 17.6623 | 18.5753 | 21.5394 | 315.7026 | 1923.5775
Escape VC | 15.5752 | 15.6233 | 15.7048 | 15.8131 | 15.9396 | 16.0591 | 16.2462 | 16.4812 | 16.783 | 17.2527 | 18.2541 | 33231.5946 | 33231.5946 | 33231.5946 | 33231.5946 | 33231.5946 | 33231.5946
MinBD | 15.8822 | 16.2689 | 16.9301 | 17.6423 | 18.6231 | 19.4263 | 20.2295 | 23.038 | 30.0885 | 84.4955 | 312.8131 | 599.5068
SPIN | 15.5701 | 15.6176 | 15.7028 | 15.813 | 15.9388 | 16.0531 | 16.2225 | 16.4123 | 16.6399 | 16.9319 | 17.2708 | 17.7315 | 18.3908 | 19.5163 | 32.0144 | 31329.6118 | 31329.6118
SWAP-1 | 15.5828 | 15.6373 | 15.7268 | 15.839 | 15.9757 | 16.0997 | 16.2784 | 16.4862 | 16.7386 | 17.0604 | 17.4485 | 17.9603 | 18.6452 | 19.753 | 23.1284 | 36508.9513 | 36508.9513
SWAP-16K | 15.5639 | 15.6432 | 15.7293 | 15.8376 | 15.9602 | 16.1098 | 16.2829 | 16.4918 | 16.7433 | 17.0514 | 17.4379 | 17.9416 | 18.636 | 19.7183 | 13513.2379 | 259794.8037
Chart: Shuffle
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34
XY | 13.0558 | 13.0907 | 13.1338 | 13.1857 | 13.2572 | 13.3527 | 13.4913 | 13.7032 | 14.1331 | 17.0149 | 570.793
Escape-VC-AdaptiveWestFirst | 13.0592 | 13.1007 | 13.1489 | 13.2071 | 13.2847 | 13.385 | 13.5215 | 13.7139 | 14.1138 | 1076.4487
MinBD | 13.3122 | 13.6823 | 14.1391 | 14.7234 | 15.5028 | 16.7458 | 17.7524 | 18.7589 | 23.0007 | 48.5235 | 167.838
SPIN- AdaptiveRandom dd=128 | 13.0574 | 13.0967 | 13.1439 | 13.1984 | 13.266 | 13.345 | 13.4448 | 13.5535 | 13.6923 | 13.8521 | 14.0539 | 14.3183 | 14.6688 | 15.239 | 16.5012 | 113.4077 | 870.2601
SWAP-1-AdaptiveRand | 13.0609 | 13.1031 | 13.1536 | 13.2118 | 13.2859 | 13.3742 | 13.485 | 13.6117 | 13.7724 | 13.9637 | 14.1999 | 14.5098 | 14.9139 | 15.5276 | 16.7302 | 211.4464
SWAP-16384 AdaptiveRand occupany-0 | 13.1031 | 13.1536 | 13.2118 | 13.2859 | 13.3742 | 13.485 | 13.6117 | 13.7727 | 13.9667 | 14.207 | 14.5093 | 14.9141 | 15.5374 | 16.7283 | 238.6929
Chart: Bit-Rotation
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4
XY | 13.051 | 13.0854 | 13.1243 | 13.1798 | 13.253 | 13.3505 | 13.4851 | 13.7022 | 14.1118 | 15.4094 | 222.9569 | 1765.7346
Escape-VC-AdaptiveWestFirst | 13.0483 | 13.0811 | 13.1133 | 13.1599 | 13.214 | 13.2788 | 13.3538 | 13.4503 | 13.5633 | 13.7086 | 13.9047 | 14.1963 | 14.857 | 451.2305 | 7004.3256
MinBD | 13.2981 | 13.6267 | 14.0446 | 14.5874 | 15.3672 | 16 | 17.2312 | 18.4623 | 22.3217 | 39.0607 | 140.9684 | 377.7132
SPIN- AdaptiveRandom dd=128 | 13.0495 | 13.0816 | 13.1154 | 13.1609 | 13.2154 | 13.2754 | 13.3435 | 13.4228 | 13.514 | 13.6225 | 13.7498 | 13.8982 | 14.0743 | 14.3065 | 14.624 | 15.1459 | 38.4777 | 11433.4106
SWAP-1-AdaptiveRand | 13.0494 | 13.0812 | 13.113 | 13.1559 | 13.2109 | 13.27 | 13.3381 | 13.4191 | 13.5107 | 13.6214 | 13.7542 | 13.9047 | 14.0948 | 14.3256 | 14.6274 | 15.0505 | 15.7366 | 27.4962 | 441.3121 | 5725.9648
SWAP-16384 AdaptiveRand occupany-0 | 13.0494 | 13.0812 | 13.113 | 13.1559 | 13.2109 | 13.27 | 13.3381 | 13.4191 | 13.5107 | 13.6214 | 13.7542 | 13.9047 | 14.0924 | 14.3242 | 14.6224 | 15.0476 | 15.7277 | 20.0203 | 447.6421 | 3331.977
Chart: Transpose
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42
XY | 15.5575 | 15.6114 | 15.6841 | 15.7769 | 15.946 | 16.3444 | 20.0346 | 798.8233 | 1766.1309 | 261.3357 | 355.577 | 421.5013
Escape-VC | 15.5637 | 15.6248 | 15.7039 | 15.7834 | 15.8963 | 16.0469 | 16.239 | 16.5164 | 16.9731 | 18.0448 | 312.6048 | 1536.8384
MinBD | 15.8244 | 16.2145 | 16.702 | 17.342 | 18.1802 | 19.5162 | 20.6369 | 21.7577 | 27.1478 | 80 | 221.649 | 496.2207 | 750.6989
SPIN | 15.5729 | 15.6594 | 15.7633 | 15.8604 | 15.9858 | 16.14 | 16.3192 | 16.539 | 16.8094 | 17.1491 | 17.6087 | 18.3302 | 19.9587 | 346.2652
SWAP-1 | 15.5636 | 15.6224 | 15.6955 | 15.7651 | 15.8582 | 15.9875 | 16.1353 | 16.3306 | 16.576 | 16.9082 | 17.3894 | 18.1086 | 19.4192 | 47.5874 | 798.5921
SWAP-16k | 15.5636 | 15.6224 | 15.6955 | 15.7651 | 15.8582 | 15.9875 | 16.1353 | 16.3306 | 16.576 | 16.9171 | 17.3914 | 18.0929 | 19.3986 | 48.1489 | 806.4531 | 1803.0501 | 2597.2863 | 3675.4597 | 4703.0867 | 5605.3979
40% higher throughput than DoR
44% higher throughput than Deflection
25% higher throughput than Escape VC
10% higher throughput than Deadlock Detection
More results in paper

## Slide 24: Link Traversal Energy
SPIN has 8-10x higher link activity because of probes
Deflection has 60% higher link activity because of continuous misroute
SWAP has close to 0 additional link activity at higher period
More analysis in paper

## Slide 25: MESI Cache Coherence
Chart: MESI
| Barnes | canneal | Fmm | Lu_ncb | Radix | Swaptions | Average
XY | 26.727 | 17.5819 | 24.6117 | 66.2068 | 38.8499 | 20.5942 | 32.4286
WF | 26.727 | 17.6013 | 24.6117 | 66.54 | 38.6152 | 20.2565 | 32.3919
Escape VC(WF) | 26.721 | 17.6429 | 25.1482 | 72.6089 | 38.6488 | 20.4214 | 33.5318
SPIN | 12.1469 | 11.5985 | 13.0614 | 44.7937 | 12.8095 | 11.1417 | 17.5919
SWAP | 11.0641 | 11.0797 | 11.4909 | 23.8192 | 11.2436 | 11.2469 | 13.3241
Chart: MESI
| Barnes | canneal | Fmm | Lu_ncb | Radix | Swaptions | Average
XY | 1 | 1 | 1 | 1 | 1 | 1 | 1
WF | 1 | 1.0071 | 0.99213 | 0.98161 | 1.0072 | 1.0063 | 0.99907
Escape VC(WF) | 1.0092 | 0.99284 | 0.9432 | 0.9986 | 1.0036 | 1.0262 | 0.9956
SPIN | 0.86643 | 0.89526 | 0.91549 | 0.64259 | 0.82393 | 1.0505 | 0.8657
SWAP | 0.85614 | 0.91847 | 0.88035 | 0.48431 | 0.81827 | 0.96545 | 0.8205
18% speedup on average
Notes: This is directory based protocol with less network activity

## Slide 26: MOESI Cache Coherence
Chart: MOESI
| Barnes | Bodytrack | canneal | FFT | F'animate | Fmm | Lu_ncb | Ocean_cp | Streamcluster | Average
XY | 27.6243 | 27.3977 | 25.7783 | 58.5852 | 27.6314 | 30.5505 | 41.3351 | 59.7167 | 26.4915 | 36.1234
WF | 28.0961 | 27.689 | 25.94 | 77.1203 | 27.9035 | 31.0264 | 43.9969 | 65.3691 | 26.5404 | 39.298
Escape VC(WF) | 27.936 | 27.6319 | 25.9246 | 58.7932 | 27.9586 | 31.0299 | 44.1419 | 66.1561 | 26.5629 | 37.3483
SPIN | 25.9986 | 26.3546 | 25.0486 | 32.7634 | 26.4454 | 29.0533 | 39.4343 | 46.6958 | 25.3779 | 30.7969
SWAP | 19.0357 | 19.1159 | 18.7433 | 20.2894 | 19.1323 | 19.4328 | 24.1386 | 22.4519 | 18.9578 | 20.1442
Chart: MOESI
| Barnes | Bodytrack | canneal | FFT | F'animate | Fmm | Lu_ncb | Ocean_cp | Streamcluster | Average
XY | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
WF | 1.0164 | 0.996 | 1.0528 | 1.0078 | 1.0049 | 0.87576 | 0.99548 | 1.428 | 1.0036 | 1.0423
Escape VC(WF) | 0.99109 | 1.0141 | 1.0132 | 1.0075 | 1.0026 | 0.97624 | 1.0089 | 1.214 | 0.97603 | 1.0226
SPIN | 1.1397 | 0.98519 | 1.0335 | 0.98407 | 1.002 | 0.91133 | 0.93879 | 1.1982 | 0.98474 | 1.0197
SWAP | 0.97571 | 0.98531 | 0.9745 | 0.9696 | 0.99267 | 0.94637 | 0.82796 | 0.91328 | 0.88495 | 0.94115
6% speedup on average

## Slide 27: Outline
Background: Deadlocks
Current Solutions
SWAP
  Concept
  Walk-through
  Deadlock freedom proof
  Router microarch
Evaluations
  Methodology
  Results
Conclusion
Notes: Now let me introduce to you the concept of BBR and how it takes an orthogonal approach compared to prior work to resolve deadlocks

## Slide 28
Design | Resolution Type | Full Path Diversity | No Extra VCs | Topology Agnostic | No Deadlock Detection
Dally/Turn Restriction [1] | No Cycle |  |  |  | 
Duato/Escape VC [2] | Escape |  |  |  | 
Injection Restriction [3] | Bubble |  |  |  | 
Deflection [4] | Misroute |  |  |  | 
Coordination [5] | Synchronize |  |  |  | 
SWAP | Backtrack |  |  |  | 
*in all VCs except escape VC
*
Revisiting Qualitative Comparison
*
[1]:
[2]:
[3]:
[4]:
[5]:
Deadlock-free message routing in multiprocessor interconnection networks [IEEE Trans. Computer, 1987]
A new theory of deadlock-free adaptive routing in wormhole networks. [IEEE Trans. On Parallel and Dist. Sys, 1993]
Bubble Flow Control [IPDPS 2011]
BLESS [ISCA’09] CHIPPER [HPCA’11]
DISHA [IPDPS’95] Static Bubble [HPCA’17] SPIN [ISCA’18]
[6]:
SWAP [MICRO’19]

## Slide 29: Conclusion
Deadlock is the problem which every network must solve
Current solutions either require complex deadlock detection or provision extra set of buffers or restrict turns
SWAP provides a novel way of resolving deadlock by swapping packets in the network.
  No extra buffer needed as it does in-place swap
  Free from complicated deadlock detection circuitry
  Provides full path-diversity therefore high performant
Thank you!
Questions?