## Slide 1: SEEC: Stochastic Escape Express Channel
Mayank Parasar1, Natalie Enright Jerger2, Paul V. Gratz3, Joshua San Miguel4, Tushar Krishna1
Supercomputing 2021
November 16, 2021
https://github.com/noc-deadlock/seec
1
1Georgia Tech
Presented By:
Tushar Krishna
Associate Professor
School of ECE
Georgia Institute of Technology
Email: tushar@ece.gatech.edu
Email: tushar@ece.gatech.edu
2Univ of Toronto
3Texas A&M
4Univ of Wisconsin
November 16, 2021

## Slide 2: Interconnection Networks are at the heart of HPC
This work focuses on interconnection networks-on-chip (aka NoCs)

## Slide 3: Why do we need Networks-on-Chip?
Many Core
Network-on-Chip
Communication
Power Wall

## Slide 4: Network-on-Chip 101
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)
Design-time hardware-managed topology, routing and flow-control decisions makes networks-on-chip different from larger scale HPC / datacenter networks

## Slide 5: Challenges with NoC Design
Correctness  Guaranteed packet delivery
  No Routing Deadlocks
  No Protocol Deadlocks
Performance  Deliver as many packets as fast as possible
  Reduce Latency
  Increase Throughput
Challenge: Cyclic dependence
9
5
10
6
1
7
14
8
Deadlock
Challenge: Congestion
5
1
0
4
0
0
0
0
1
0
0
0
3
This work addresses both challenges with a unified solution

## Slide 6: Outline
Background
  Networks-on-Chip
  Deadlock-Freedom Techniques
SEEC
  Overview
  Walkthrough
  Features
  Optimizations
Evaluations
Conclusions

## Slide 7: What are deadlocks?
A condition in which a set of agents wait indefinitely trying to acquire a set of resources

## Slide 8: Two kinds of deadlocks
9
5
10
6
5
9
6
10
Deadlock
5
Destination Router-5
Network
Network
Network
Network
Routing Deadlocks
Finite Network Buffers
Injection queue
Ejection queue
Protocol Deadlocks
Cache
Directory
Request Packets
Response Packet
Buffers occupied by the request packets renders forward movement of response packet impossible
Deadlock

## Slide 9: Current solutions for deadlock-freedom
Proactive Techniques
  Avoid deadlock to begin with
Reactive Techniques
  Allow deadlocks to form in the network
  Detect deadlocks and recover from them
Add turn restrictions or provide additional virtual lanes/channels
Add circuitry for monitoring and identifying cyclic dependencies at runtime
Notes: We have classified the prior proposed techniques in following two categories:
Proactive Techniques: These techniques avoid the deadlock in the network to begin with
Reactive Techniques: These techniques allows the deadlock in the network. They detects the deadlock and then recovers from it.

## Slide 10: Example of proactive routing deadlock-freedom
9
5
10
6
5
9
6
10
Deadlock
5
Destination Router-5
Network
Network
Network
Network
Routing Deadlocks
9
5
10
6
5
9
6
10
Network
Network
Network
Network
X
Add turn restrictions

## Slide 11: Example of proactive protocol deadlock-freedom
Cache
Directory
Request Packet
Response Packet
Finite Network Buffers
Cache
Directory
Injection queue
Ejection queue
Dedicated Separate Queues (aka Virtual Networks)
Protocol Deadlocks
Deadlock

## Slide 12: Deadlock-Freedom Techniques
Technique | Type of Solution | High Throughput | Low Area Power | Low Hardware Complexity | Routing Deadlock-free | Protocol Deadlock-free
Turn Restriction [1] | Proactive |  |  |  |  | 
Escape VC [2] | Proactive |  |  |  |  | 
Virtual Network [3] | Proactive |  |  |  |  | 
Deadlock Recovery [4] | Reactive |  |  |  |  | 
? | ?? |  |  |  |  | 
[1]:
[2]:
[3]:
[4]:
Deadlock-free message routing in multiprocessor interconnection networks [IEEE Trans. Computer, 1987]
A new theory of deadlock-free adaptive routing in wormhole networks. [IEEE Trans. On Parallel and Dist. Sys, 1993]
The Alpha 21364 network architecture [MICRO 2002]
DISHA [IPDPS’95] Static Bubble [HPCA’17] SPIN [ISCA’18]
Takeaway:
Proactive techniques add performance and area overheads.
Reactive techniques require expensive monitoring circuitry
Can we do better?
Notes: Deadlock is a well studied problem in interconnection networks, more than 4 decades of research has been done in this field. I am evaluating the previous proposed solutions on following metric
Weather the solution provides full path diversity?
If there are extra VCs used in the solution?
Is the solution works for a fixed topology?
Does the solution require expensive circuitry to detect and resolve deadlock?
--
Dally’s solution restricts certain turns that a packet can take in the network, so the packet is not involved in the deadlock, to begin with.
Because of turn restriction, a packet cannot utilize the full path diversity and it needs to know about the topology.
Duato’s theory proposes an acyclic escape path within the extended cyclic CDG of the network and every packet has access to this acyclic escape path to make the network deadlock-free. Acyclic escape path requires an extra set of buffers in the form of escape VC and escapeVC needs to know about the topology to make this escape path acyclic, and packet in the escape path cannot enjoy the full path diversity
Then there is work on restricting the injection of packets in the network such that deadlock never happens. This comes with an underlying theory that as long as there is a bubble or free VC present in the ring it will be deadlock-free.
This cannot provide full path diversity to the packet and this theory is tied to ring-like topology
Deflection routing keeps misrouting packets every cycle such that the packet never stays in the same buffer for more that one cycle. Because of which packet cannot utilize the full path diversity during congestion due to continued misrouting.
Then there is work on coordination, which detects and maps the deadlock during runtime using probes and timeouts and then synchronizes the movement of packets involved in the deadlock. This involves complicated deadlock detection circuitry.
As we can see there is no work which has all the favorable characteristics and we ask this question that can we come up with a technique which provides all these favorable characteristics

## Slide 13: “Subactive” Techniques
Proactive Techniques
  Avoid deadlock to begin with
Reactive Techniques
  Allow deadlock to form in the network
  Detect deadlocks and recover from them
Subactive Techniques
  Allow deadlocks to form in the network
  Obliviously flush network to remove any deadlock
Notes: We introduce a new class of solutions called ”Subactive Techniques”
These techniques allows the deadlock in the network, but oblivious flushes the network to remove any deadlock which may be present.

## Slide 14: Intuition behind Subactive
Deadlocks are rare!
  Requires certain ensemble of packets with a particular buffer dependency for the deadlock to occur
A mechanism to ensure periodic draining of packets sufficient to guarantee deadlock-freedom
  No need for proactive performance restrictions / additional reserved queues
  No need for detection and reactive recovery
This work (SEEC) is one of many possible subactive solutions
  See our other work: SWAP (MICRO 2019), DRAIN (HPCA 2020), PitStop (HPCA 2021)

## Slide 15: Outline
Background
  Networks-on-Chip
  Deadlock-Freedom Techniques
SEEC
  Overview
  Walkthrough
  Features
  Optimizations
Evaluations
Conclusions

## Slide 16: SEEC: Deadlock Analogy
Deadlock
Destination

## Slide 17: SEEC: Walk-through for Deadlock-freedom
9
5
10
6
2
3
1
13
14
15
11
7
0
4
8
12
1
7
14
8
Upgrade to FF
Seeker
Upgrade to FF
Deadlock
S
E
W
N
Seeker Path
Seeker
Free Slot
1
Reserve a free ejection buffer at the NIC
Send a seeker over a sideband seeker path through all routers
If a packet intended for this NIC is found, upgrade it for Free Flow (FF)
FF packet given priority over regular packets to traverse all the way to the N
Repeat for all NICs in round-robin manner
5
Destination Router-5
NIC

## Slide 18: Outline
Background
  Networks-on-Chip
  Deadlock-Freedom Techniques
SEEC
  Overview
  Walkthrough
  Features
  Optimizations
Evaluations
Conclusions

## Slide 19: Features of SEEC
Novel Flow Control: Free Flow (FF)
  Packets upgraded to FF via seeker
  FF packet gets prioritized over the buffered packets
    FF packet sends a lookahead signal on cycle in advance
    lookahead signal sets the appropriate mux at downstream router
    FF packet traverse the network from link to link till the NIC
  FF packets follow minimal (shortest) express path with no buffering
  SEEC proposes co-existence of FF packets and buffered packets
Seeker Path
  Any pre-defined path that visits all routers
  Separate sideband network
    could use regular links by prioritizing seeker over regular packets
  Possible to have multiple parallel seekers  later in talk

## Slide 20: Router Microarchitecture
FF packet Bypass Path

## Slide 21: Deadlock Freedom Proof
The ejection port at NIC has separate Virtual Networks (one per protocol message class)
The response packet can cause a protocol deadlock, if stuck in network
SEEC is protocol deadlock free as NIC will eject any blocked response packet by sending seeker
SEEC is routing deadlock free as all the input ports get chance to send packets via FF flow control
SEEC is livelock free as there is no misrouting

## Slide 22: Mathematical upper bound for deadlock persistence
For any irregular network topology:
  Assume diameter is D
  Assume it takes on an average ‘k’ cycles at the ejection port
  Number of nodes in the network is ‘N’
  Let the average network router-radix of the router is ‘r’
The maximum time it takes for a deadlock to persist
  Deadlock involves at least 4 routers
  [{r*(N-4)*2*D*k} + (D+k)] cycles

## Slide 23: SEEC: Additional Benefits  Performance
SEEC helps packets to bypass congestion in the network, improving performance
9
5
10
6
2
3
1
13
14
15
11
7
0
4
8
12
0
0
0
0
1
0
0
0
Seeker
Free Slot
1
NIC
Upgrade to FF
0
3
Congestion
Blocked!

## Slide 24: Outline
Background
  Networks-on-Chip
  Deadlock-Freedom Techniques
SEEC
  Overview
  Walkthrough
  Features
  Optimizations
Evaluations
Conclusions

## Slide 25: Multi-SEEC (mSEEC)
Motivation
  Path Diversity in many topologies: Multiple ways of reaching a node
Features of mSEEC
  Creates multiple FF packets that can traverse simultaneously
Requirement
  Multiple FF packets traverse minimally without overlapping paths
Implementation
  mSEEC divides the topology into independent regions

## Slide 26: mSEEC: Walk Through
When Phase-0 finishes:
  each node in group-0 has searched entire topology
Phase-1 starts
A
B
C
D
E
F
G
H
I
0
1
2
Partition
Group-0
A
B
C
D
E
F
G
H
I
0
1
2
A
B
C
D
E
F
G
H
I
0
1
2
Seeker
Packet
Phase 0

## Slide 27: mSEEC: Walk Through
When Phase-1 finishes:
  each node in group-1 has searched entire topology
Phase-2 starts and so on…
A
B
C
D
E
F
G
H
I
0
1
2
Partition
Group-1
A
B
C
D
E
F
G
H
I
0
1
2
A
B
C
D
E
F
G
H
I
0
1
2
Seeker
Packet
Phase 1

## Slide 28: Outline
Background
  Networks-on-Chip
  Deadlock-Freedom Techniques
SEEC
  Overview
  Walkthrough
  Features
  Optimizations
Evaluations
Conclusions

## Slide 29: Evaluations Methodology
gem5 for full system and synthetic simulations
Garnet2.0 for network simulation
SEEC/mSEEC uses minimal adaptive routing algorithm with full path diversity
Virtual Cut Through Buffer Management
Evaluated on 4x4 (16 nodes), 8x8 (64 nodes), and 16x16 (256 nodes) Mesh topology

## Slide 30: Results: Performance Sweep
Chart: 4x4 Mesh Shuffle
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5 | 0.52 | 0.54 | 0.56000000000000005 | 0.57999999999999996 | 0.6 | 0.62
XY | 9.0073 | 9.0117 | 9.0159 | 9.0193 | 9.0265 | 9.0346 | 9.0443 | 9.0551 | 9.0636 | 9.077 | 9.0947 | 9.1146 | 9.1365 | 9.1631 | 9.1943 | 9.2318 | 9.2786 | 9.3376 | 9.4169 | 9.5248 | 9.6841 | 9.9546 | 10.483 | 12.0593 | 69.818 | 975.3691 | 1798.2586 | 2539.7275 | 3204.4234 | 3799.5834 | 4324.7271
WestFirst | 9.0079 | 9.0137 | 9.0197 | 9.0242 | 9.0322 | 9.0413 | 9.0531 | 9.0672 | 9.0766 | 9.092 | 9.1115 | 9.1329 | 9.1587 | 9.1902 | 9.2237 | 9.2655 | 9.3191 | 9.3778 | 9.4705 | 9.5893 | 9.7777 | 10.1506 | 11.0383 | 59.2888 | 324.9363 | 830.6292 | 1257.7241 | 1628.678 | 2036.7977 | 2376.0309 | 2919.3188
EscapeVC | 9.0088 | 9.0156 | 9.0251 | 9.0301 | 9.0391 | 9.0512 | 9.0626 | 9.0789 | 9.0893 | 9.1062 | 9.1282 | 9.1518 | 9.1776 | 9.2073 | 9.243 | 9.285 | 9.331 | 9.3825 | 9.4513 | 9.5414 | 9.6406 | 9.8043 | 10.0612 | 10.4795 | 11.7632 | 167.4862 | 384.1705 | 773.2326 | 1328.6097 | 1868.8782 | 2541.8906
SPIN | 9.0073 | 9.0117 | 9.0159 | 9.0193 | 9.0265 | 9.0346 | 9.0443 | 9.0551 | 9.0637 | 9.0771 | 9.0948 | 9.1147 | 9.1366 | 9.1633 | 9.1947 | 9.232 | 9.2793 | 9.3385 | 9.4188 | 9.5289 | 9.6906 | 9.9701 | 10.5267 | 12.3112 | 133.5509 | 985.902 | 1682.2878 | 2250.1111 | 2697.8692 | 3055.4757 | 3453.0847
SWAP | 9.0097 | 9.0171 | 9.0242 | 9.0298 | 9.0412 | 9.0511 | 9.0649 | 9.0794 | 9.0902 | 9.1081 | 9.1295 | 9.1535 | 9.1793 | 9.2062 | 9.2364 | 9.2747 | 9.313 | 9.3551 | 9.4051 | 9.4635 | 9.5308 | 9.6084 | 9.7127 | 9.8418 | 10.0237 | 10.3427 | 11.0094 | 29.4089 | 330.8975 | 618.5831 | 857.483
DRAIN | 9.0041 | 9.0452 | 9.0531 | 9.0591 | 9.0685 | 9.0784 | 9.0887 | 9.1019 | 9.1128 | 9.1282 | 9.1458 | 9.169 | 9.1914 | 9.2146 | 9.2438 | 9.2746 | 9.3115 | 9.3496 | 9.3958 | 9.4439 | 9.5074 | 9.568 | 9.6626 | 9.772 | 9.9306 | 10.1873 | 10.8259 | 50.9292 | 106.0356 | 192.0124 | 200.2222
SEEC | 9.0094 | 9.0159 | 9.0226 | 9.0287 | 9.0391 | 9.0496 | 9.0625 | 9.0756 | 9.0872 | 9.1036 | 9.1222 | 9.1449 | 9.1674 | 9.1938 | 9.2219 | 9.2548 | 9.2902 | 9.3261 | 9.3691 | 9.4202 | 9.479 | 9.5466 | 9.63 | 9.7429 | 9.8968 | 10.1308 | 10.6161 | 13.2583 | 209.0278 | 484.0463 | 705.0305
mSEEC | 9.0064 | 9.0102 | 9.0142 | 9.0187 | 9.0248 | 9.0327 | 9.0421 | 9.0531 | 9.0608 | 9.0732 | 9.0882 | 9.1056 | 9.1246 | 9.1405 | 9.1635 | 9.1885 | 9.2135 | 9.2409 | 9.2735 | 9.3082 | 9.347 | 9.3952 | 9.4468 | 9.5156 | 9.598 | 9.6945 | 9.8242 | 10.0256 | 10.3918 | 11.8263 | 89.9882
Chart: 8x8 Mesh Shuffle
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46
XY | 13.0555 | 13.0904 | 13.1326 | 13.1832 | 13.2529 | 13.3445 | 13.4776 | 13.6767 | 14.051 | 15.005 | 24.3331 | 2344.5924 | 4387.8568 | 6009.6388 | 7149.3184 | 8187.375
WestFirst | 13.0569 | 13.0968 | 13.1427 | 13.1984 | 13.2751 | 13.3746 | 13.5233 | 13.7657 | 14.463 | 270.7534 | 3369.2477 | 4936.4574 | 5578.4071 | 6248.9391 | 6749.3591 | 7318.3032
EscapeVC | 13.0594 | 13.1003 | 13.1468 | 13.2036 | 13.2798 | 13.3764 | 13.5083 | 13.6964 | 3253.6677 | 6170.2839 | 7203.8125 | 8383.5611 | 8847.5037 | 9478.3958 | 10157.5422 | 10361.371
SPIN | 13.0558 | 13.0907 | 13.1338 | 13.1855 | 13.2577 | 13.3535 | 13.4921 | 13.7072 | 14.143 | 17.132 | 571.8515 | 1677.1668 | 2783.9625 | 4130.6942 | 4838.5402 | 5528.292
DRAIN | 13.1091 | 13.1486 | 13.1979 | 13.2536 | 13.324 | 13.4066 | 13.51 | 13.6256 | 13.7715 | 13.948 | 14.1642 | 14.4488 | 14.8437 | 15.5409 | 17.6302 | 257.0386 | 623.0671 | 828.7812 | 977.2559 | 1063.6576 | 1077.9888 | 1092.9766 | 1156.2063 | 1211.0887 | 1299.6186
SWAP | 13.0609 | 13.1031 | 13.1536 | 13.2118 | 13.2858 | 13.3743 | 13.4859 | 13.611 | 13.7757 | 13.9621 | 14.1993 | 14.5106 | 14.9136 | 15.5272 | 16.6764 | 157.4206
SEEC | 13.0605 | 13.1033 | 13.152 | 13.2073 | 13.2783 | 13.3635 | 13.4659 | 13.5809 | 13.7306 | 13.8989 | 14.1105 | 14.3855 | 14.7445 | 15.2674 | 16.2619 | 198.5061 | 1773.2761 | 3126.1223 | 4752.9684
mSEEC | 13.043 | 13.0658 | 13.0945 | 13.1278 | 13.1724 | 13.2257 | 13.2889 | 13.3556 | 13.439 | 13.5294 | 13.6343 | 13.752 | 13.8868 | 14.0473 | 14.2221 | 14.4289 | 14.675 | 14.969 | 15.3324 | 15.8099 | 16.513 | 17.8262 | 64.4376 | 755.9479 | 1752.0984
Chart: 16x16 Mesh Shuffle
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
XY | 21.1079 | 21.2553 | 21.4886 | 21.9718 | 39.0045 | 3665.7192 | 3892.7815 | 4842.7744 | 4544.0189 | 6252.2716
WestFirst | 21.1381 | 21.3358 | 21.6587 | 23.8373 | 2434.7214 | 4649.9591 | 4704.7817 | 5384.3543 | 5103.5599 | 6353.5247
EscapeVC | 21.1455 | 21.358 | 21.6998 | 651.6404 | 6778.2685 | 5975.6013 | 7752.6127 | 7188.3503 | 8377.4474 | 8165.1975
SPIN | 21.1083 | 21.2582 | 21.499 | 21.971 | 121.4896 | 2892.7109 | 4318.4847 | 5558.4027 | 6853.3961 | 7351.6657
SWAP | 21.1693 | 21.4019 | 21.7432 | 22.2327 | 22.9878 | 24.2157 | 1598.1542 | 4062.4437 | 4158.3274 | 4537.8115
DRAIN | 21.2247 | 21.4471 | 21.7639 | 22.2082 | 22.8546 | 23.885 | 27.7587 | 5053.6317 | 5593.5508 | 5202.0516 | 5219.5427
SEEC | 21.1661 | 21.3916 | 21.7125 | 22.1619 | 22.8279 | 23.8961 | 26.4163 | 1999.086 | 1990.0457 | 1956.4885 | 2084.377
mSEEC | 21.087 | 21.2145 | 21.3903 | 21.6067 | 21.8774 | 22.1946 | 22.5753 | 23.0292 | 23.61 | 24.6179 | 18329.7871
11% over subactive techniques
25% over prior work
30% over subactive techniques
40% over prior work
40% over subactive techniques
57% over prior work

## Slide 31: Results: Throughput Enhancement
Chart: Saturation Throughput
| 4x4 Mesh | 8x8 Mesh | 16x16 Mesh
XY | 0.12 | 0.08 | 0.04
SWAP-XY | 0.12 | 0.08 | 0.04
SEEC-XY | 0.14 | 0.08 | 0.04
Uniform Random
XY Routing
Chart: Saturation Throughput
| 4x4 Mesh | 8x8 Mesh | 16x16 Mesh
WF | 0.12 | 0.06 | 0.02
SWAP-WF | 0.12 | 0.06 | 0.02
SEEC-WF | 0.14 | 0.06 | 0.02
Uniform Random
West First Routing
16% throughput improvement in 4x4 Mesh

## Slide 32: Results: SEEC-%age of FF packets
Chart: Uniform Random 8x8 Mesh VC-2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
Bufferless pkt | 2.2889 | 5.0467 | 7.921 | 10.3565 | 11.8548 | 45.5702 | 95.8318 | 96.6899 | 96.1857 | 96.821 | 96.8652
Chart: Transpose 8x8 Mesh VC-2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
Bufferless pkt | 1.5625 | 3.72 | 6.2292 | 8.5301 | 10.5557 | 11.5596 | 11.1537 | 10.3842 | 9.8012 | 9.3152 | 8.9143
Chart: Bit Complement 8x8 Mesh VC-2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
Bufferless pkt | 7.5231 | 17.32 | 98.8496 | 99.5658 | 99.8472 | 99.8771 | 99.8452 | 99.939 | 99.8452 | 99.928 | 99.9241
Post saturation heavy reliance on FF for packet delivery

## Slide 33: Results: Full System Simulation
Chart: MOESI-hammer
| Bodytrack | canneal | FFT | Fmm | Lu_cb | Ocean_cp | Volrend | Average
EscapeVC | 29.2979 | 29.4994 | 43.6821 | 32.7665 | 27.9085 | 79.6328 | 27.0051 | 38.5418
SPIN | 26.3546 | 25.0486 | 32.7634 | 29.0533 | 25.3781 | 46.6958 | 24.702 | 29.9994
BBR | 34.9794 | 41.1316 | 59.3491 | 43.5212 | 33.1161 | 76.1526 | 30.3497 | 45.5143
BINDU | 30.933 | 32.0144 | 64.3009 | 35.7084 | 28.5212 | 63.8707 | 27.34 | 40.3841
SWAP | 27.6642 | 27.5465 | 40.8853 | 32.1812 | 26.3764 | 52.7619 | 25.5965 | 33.2874
DRAIN | 30.9348 | 26.2545 | 46.4669 | 35.1087 | 27.7605 | 59.3914 | 26.3159 | 36.0333
SEEC | 25.5776 | 26.5732 | 35.5779 | 28.9017 | 24.9353 | 42.08 | 24.2754 | 29.703
mSEEC | 22.8178 | 24.4046 | 27.2993 | 25.4785 | 23.2531 | 30.0848 | 22.7991 | 25.1624
mSEEC provides 37% lower packet latency compared to baseline Escape VC in 4x4 Mesh

## Slide 34: Normalized Area and Static Power
Chart: 
| Area | Power
Escape VCs | 1 | 1
SPIN | 0.86277 | 0.85627
SWAP | 0.82168 | 0.82333
DRAIN | 0.41813 | 0.35775
SEEC | 0.39822 | 0.34071
~70% Lower Static Power
~65% Lower Static Area
Notes: Major Area/power savings comes from lower buffer overhead.

## Slide 35: Outline
Background
  Networks-on-Chip
  Deadlock-Freedom Techniques
SEEC
  Overview
  Walkthrough
  Features
  Optimizations
Evaluations
Conclusions

## Slide 36: Conclusion
Deadlock is a correctness problem which every network must solve
Current solutions either require complex deadlock detection or provision extra set of buffers or restrict turns
SEEC provides a novel way of resolving deadlock by periodically moving packets for few hops along a ring constructed over the network.
  No extra buffer needed
  Free from complicated deadlock detection circuitry
  Provides full path-diversity therefore high performant

## Slide 37: Revisiting Qualitative Comparison
Teechnique | Type of Solution | High Throughput | Low Area Power | Low Hardware Complexity | Routing Deadlock-free | Protocol Deadlock-free
Turn Restriction | Proactive |  |  |  |  | 
Escape VC | Proactive |  |  |  |  | 
Virtual Network | Proactive |  |  |  |  | 
Deadlock Recovery | Reactive |  |  |  |  | 
SEEC | Subactive |  |  |  |  | 
Takeaways
SEEC obliviously provides deadlock freedom
SEEC is completely decentralized
SEEC has low hardware overhead over baseline router
Codebase available here:
https://github.com/noc-deadlock/seec
Thanks!
Notes: Instead of citation put take away from DRAIN
Deadlock is a well studied problem in interconnection networks, more than 4 decades of research has been done in this field. I am evaluating the previous proposed solutions on following metric
Weather the solution provides full path diversity?
If there are extra VCs used in the solution?
Is the solution works for a fixed topology?
Does the solution require expensive circuitry to detect and resolve deadlock?
--
Dally’s solution restricts certain turns that a packet can take in the network, so the packet is not involved in the deadlock, to begin with.
Because of turn restriction, a packet cannot utilize the full path diversity and it needs to know about the topology.
Duato’s theory proposes an acyclic escape path within the extended cyclic CDG of the network and every packet has access to this acyclic escape path to make the network deadlock-free. Acyclic escape path requires an extra set of buffers in the form of escape VC and escapeVC needs to know about the topology to make this escape path acyclic, and packet in the escape path cannot enjoy the full path diversity
Then there is work on restricting the injection of packets in the network such that deadlock never happens. This comes with an underlying theory that as long as there is a bubble or free VC present in the ring it will be deadlock-free.
This cannot provide full path diversity to the packet and this theory is tied to ring-like topology
Deflection routing keeps misrouting packets every cycle such that the packet never stays in the same buffer for more that one cycle. Because of which packet cannot utilize the full path diversity during congestion due to continued misrouting.
Then there is work on coordination, which detects and maps the deadlock during runtime using probes and timeouts and then synchronizes the movement of packets involved in the deadlock. This involves complicated deadlock detection circuitry.
As we can see there is no work which has all the favorable characteristics and we ask this question that can we come up with a technique which provides all these favorable characteristics

## Slide 38: Backup

## Slide 39: Results: SEEC-Network Latency breakdown
Chart: Uniform Random 8x8 Mesh VC-2
| Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12
Buffered | 13.5289 | 9.3383 | 13.5506 | 9.2854 | 13.6494 | 9.376 | 13.8623 | 9.5084 | 14.2783 | 9.9191 | 79.1606 | 140.2012
Bufferless | 0 | 8.0814 | 0 | 8.3567 | 0 | 8.46 | 0 | 8.5756 | 0 | 8.6957 | 0 | 11.6904
Chart: Transpose 8x8 Mesh VC-2
| Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14 | 0.16 | 0.18 | 0.2 | 0.22
Buffered | 13.4985 | 8.7134 | 13.5 | 8.9645 | 13.533 | 9.1119 | 13.6167 | 9.2506 | 13.851 | 9.5884 | 14.5134 | 10.2677 | 18.3957 | 14.584 | 22.4618 | 21.5759 | 22.7639 | 22.662 | 22.916 | 23.2239 | 22.7319 | 23.1842
Bufferless | 0 | 10.8642 | 0 | 10.7054 | 0 | 10.7029 | 0 | 10.8344 | 0 | 11.0355 | 0 | 11.5925 | 0 | 15.3489 | 0 | 17.1645 | 0 | 16.5308 | 0 | 16.1244 | 0 | 15.9175

## Slide 40: Result: Max Packet Latency
Chart: Max Packet Latency
| Canneal | FMM | Lu_cb | Ocean_cp | Radix | Average
XY | 1493 | 1703 | 787 | 4490 | 1481 | 1990.8
WF | 1416 | 1413 | 674 | 4160 | 1302 | 1793
Escape-VC | 637 | 1354 | 523 | 2831 | 2865 | 1642
SPIN | 399 | 6336 | 1280 | 33280 | 3456 | 8950.2
SWAP | 858 | 1498 | 622 | 5688 | 1112 | 1955.6
DRAIN | 192954 | 327414 | 86451 | 1728 | 233976 | 168504.6
SEEC | 212 | 665 | 171 | 4315 | 306 | 1133.8
mSEEC | 52 | 56 | 37 | 94 | 50 | 57.8
mSEEC has the lowest max packet latency

## Slide 41: Results: Subactive Techniques
Chart: Bit Complement 8x8 Mesh VC=2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34
BBR | 22.4528 | 640.5844 | 663.2657 | 637.6628 | 462.9275 | 600.8848 | 604.0454 | 582.6279 | 587.8447 | 574.8433 | 586.8418 | 518.9514 | 580.2018 | 550.0117 | 574.8601 | 549.4612 | 532.0994
BINDU | 21.4983 | 22.9027 | 728.6863 | 261.47 | 283.6297 | 239.0941 | 602.0095 | 597.038 | 220.9842 | 641.6991 | 469.3507 | 332.6237 | 710.8542 | 389.3648 | 693.4012 | 234.9377 | 585.1371
DRAIN | 21.2958 | 21.9518 | 85.464 | 33515.5054 | 36692.763 | 34247.7289 | 32969.2355 | 33525.5456 | 32644.2589 | 33020.6434 | 34469.4015 | 34977.8332 | 36490.4751 | 34648.8588 | 36686.3535 | 38061.4223 | 34256.7703
SWAP | 21.4773 | 22.9564 | 33746.6242 | 40146.0406 | 40727.0959 | 42372.8007 | 44712.1298 | 44975.8492 | 44025.2371 | 47184.584 | 47446.4747 | 46388.3488 | 47088.9337 | 48059.3598 | 48123.1132 | 47196.7391 | 47993.5431
SEEC | 21.2764 | 21.9302 | 23.326 | 27547.6071 | 33249.7922 | 35472.9673 | 38714.9651 | 39896.697 | 41388.9331 | 42115.4253 | 43064.8846 | 43648.2171 | 43668.2254 | 44360.8639 | 44860.515 | 45037.5642 | 45392.3418
mSEEC | 21.2691 | 21.8018 | 22.4385 | 23.1177 | 23.8476 | 24.6655 | 25.7458 | 27.7884 | 13286.691 | 16812.2474 | 19984.6685 | 22569.8998 | 24806.4506 | 26516.5025 | 28386.6067 | 29515.4552 | 30769.9256
Chart: Transpose 8x8 Mesh VC=2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5 | 0.52 | 0.54 | 0.56000000000000005 | 0.57999999999999996 | 0.6 | 0.62 | 0.64 | 0.66 | 0.68 | 0.7
BBR | 15.9217 | 16.3999 | 16.9714 | 17.7934 | 19.4091 | 126.6818 | 877.9103 | 779.7109 | 820.0087 | 837.9207 | 843.0287 | 837.3516 | 826.7579 | 814.2371 | 804.2334 | 798.7732 | 793.907 | 788.1835 | 786.5536 | 780.7381 | 766.0131 | 755.1669 | 741.1364 | 729.7806 | 722.2595 | 712.1193 | 704.5235 | 699.3458 | 690.6539 | 684.6211 | 678.202 | 675.4782 | 664.5663 | 665.5888 | 657.1621
BINDU | 15.6134 | 15.8044 | 16.0639 | 16.4391 | 17.0228 | 18.1931 | 21.9167 | 148.75 | 479.2597 | 848.5371 | 758.2603 | 716.8537 | 727.14 | 739.3134 | 755.6733 | 765.2637 | 764.4449 | 766.4062 | 765.5099 | 768.8056 | 776.8089 | 780.5272 | 779.3986 | 770.2139 | 760.3335 | 748.1296 | 740.453 | 732.4474 | 723.7913 | 717.0035 | 708.7559 | 703.1825 | 697.0267 | 692.865 | 686.4777
DRAIN | 15.6491 | 15.7747 | 15.9491 | 16.1922 | 16.5827 | 17.3446 | 20.2811 | 697.4648 | 1406.6828 | 1928.1332 | 2411.5861 | 2908.6597 | 3134.9599 | 3389.3409 | 3566.8285 | 3638.9103 | 3725.4782 | 3793.4147 | 3829.3382 | 3948.2593 | 4347.6867 | 4432.2719 | 4470.7359 | 4486.8644 | 4501.3572 | 4514.6975 | 4522.433 | 4527.2057 | 4531.9939 | 4540.0101 | 4540.4332 | 4547.2904 | 4549.1536 | 4553.1139 | 4557.2806
SWAP | 15.6071 | 15.7849 | 16.0593 | 16.4645 | 17.1039 | 18.3055 | 22.0823 | 1106.1126 | 2721.4371 | 4584.6542 | 6235.4717 | 8104.943 | 9862.2823 | 11467.4908 | 13005.6201 | 14309.2156 | 15546.0769 | 16571.4341 | 17476.6181 | 18329.3126 | 19767.3612 | 21152.6855 | 22418.6733 | 23563.4656 | 24607.4217 | 25577.3229 | 26493.9087 | 27329.2667 | 28110.4685 | 28825.3544 | 29505.4782 | 30134.045 | 30733.8365 | 31294.8268 | 31857.7866
SEEC | 15.5814 | 15.7021 | 15.8749 | 16.0975 | 16.4237 | 16.9467 | 17.9345 | 20.7378 | 823.5735 | 2445.9671 | 4548.5479 | 6155.8812 | 7637.1706 | 9421.385 | 10951.4891 | 12402.5567 | 13619.6463 | 14910.3634 | 16048.2802 | 17060.8319 | 18583.2317 | 20009.6525 | 21321.1444 | 22507.0161 | 23618.5823 | 24624.7837 | 25567.0922 | 26439.366 | 27231.8429 | 27986.045 | 28691.6854 | 29355.1715 | 29987.7801 | 30574.462 | 31127.4333
mSEEC | 15.5803 | 15.6987 | 15.8593 | 16.0362 | 16.2517 | 16.5037 | 16.7937 | 17.1239 | 17.5061 | 17.9886 | 18.6103 | 19.5753 | 21.406 | 36.0802 | 898.282 | 2272.0299 | 3842.1176 | 5667.1212 | 7502.3504 | 9148.9749 | 11048.9892 | 12826.0264 | 14453.3476 | 15922.0157 | 17286.9949 | 18555.3267 | 19713.3387 | 20793.4563 | 21803.1469 | 22733.1789 | 23608.8054 | 24425.0569 | 25206.9967 | 25931.5512 | 26617.4601
Chart: Uniform Random 8x8 Mesh VC=2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4
BBR | 15.9429 | 16.4113 | 17.1044 | 17.9977 | 19.9062 | 484.3102 | 505.0849 | 491.1155 | 496.9902 | 473.6292 | 475.9132 | 519.8829 | 528.1627 | 460.0706 | 472.3287 | 506.6123 | 481.2528 | 445.5004 | 472.341 | 473.4933
BINDU | 15.6173 | 15.7951 | 16.1741 | 16.623 | 17.3659 | 18.674 | 103.1612 | 127.0641 | 124.04 | 143.5983 | 221.9715 | 240.5194 | 154.149 | 356.4829 | 158.8871 | 295.6462 | 193.7816 | 219.9823 | 199.4793 | 307.54
DRAIN | 15.6653 | 15.7827 | 15.9931 | 16.3122 | 16.791 | 17.5758 | 2160.6061 | 37973.2451 | 39464.2115 | 39720.1249 | 42054.685 | 39312.0802 | 41648.8612 | 40557.7296 | 42647.4724 | 43024.2053 | 40377.0225 | 42078.6559 | 41756.0966 | 41059.9273
SWAP | 15.6296 | 15.8228 | 16.1512 | 16.6446 | 17.3744 | 18.6301 | 22262.2322 | 39891.3744 | 41560.8345 | 43117.6786 | 44527.6272 | 43182.253 | 43921.889 | 43931.1717 | 44220.944 | 46747.455 | 43196.0839 | 45633.444 | 45760.9852 | 45790.3762
SEEC | 15.5984 | 15.7198 | 15.9196 | 16.2105 | 16.6395 | 17.2791 | 18.524 | 36873.4951 | 42438.7098 | 43622.2835 | 44719.6244 | 44944.6621 | 44760.715 | 45896.1311 | 46098.297 | 45601.6594 | 46789.1409 | 46593.6131 | 46600.3914 | 46936.2476
mSEEC | 15.5977 | 15.7152 | 15.8948 | 16.1142 | 16.3701 | 16.6326 | 16.9497 | 17.3149 | 17.731 | 18.2714 | 18.9733 | 20.1198 | 22.6315 | 3508.3067 | 7040.6321 | 9884.5694 | 12173.4371 | 14287.5092 | 16269.5302 | 17876.7569
We observe following performance order (subactive techniques only) : BBR < BINDU ≈ DRAIN ≈ SWAP < SEEC < mSEEC