## Slide 1: Subactive Techniques for Guaranteeing Routing and Protocol Deadlock Freedom in Interconnection Networks
Mayank Parasar
Ph.D. Defense
School of Electrical and Computer Engineering
Georgia Institute of Technology
mparasar3@gatech.edu

## Slide 2: Acknowledgement
Committee Members
  Dr. Tushar Krishna, Assistant Professor, ECE, Ph.D. Advisor
  Dr. Paul V. Gratz, Associate Professor, ECE, Texas A&M
  Dr. Hyesoon Kim, Professor, SCS
  Dr. Alexandro Daglis, Assistant Professor, SCS
  Dr. Moinuddin Qureshi, Professor, SCS
Collaborators
  Dr. Natalie Enright Jerger
  Dr. Joshua San Miguel
  Dr. Abhishek Bhattacharjee
  Dr. Arkaprava Basu
  Dr. Michael Wayne LeBeane
  Eric Van Tassell
  Sooraj Puthoor
  Hossein Farrokhbakht
  Ankit Sinha

## Slide 3: Publications
Deadlock-Freedom
  Mayank Parasar, H. Farrokhbakht, N. Enright Jerger, P. Gratz, T. Krishna, and J. San Miguel, “DRAIN: Deadlock Removal for Arbitrary Irregular Networks,” in The 26th IEEE International Symposium on High-Performance Computer Architecture (HPCA), San Diego, California, USA, Feb 2020.
  Mayank Parasar, N. Enright Jerger, P. Gratz, J. San Miguel, and T. Krishna, “SWAP: Synchronized Weaving of Adjacent Packets for Network Deadlock Prevention,” in In Proc of 52nd Annual IEEE/ACM International Symposium on Microarchitecture, MICRO-52, 2019.
  Mayank Parasar and T. Krishna, “BINDU: Deadlock-freedom with one bubble in the network,” in Proceedings of the Thirteenth IEEE/ACM International Symposium on Networks-on-Chip, NOCS, 2019.
  Mayank Parasar, A. Sinha, and T. Krishna, “Brownian Bubble Router: Enabling deadlock freedom via guaranteed forward progress,” in Proceedings of the Twelfth IEEE/ACM International Symposium on Networks-on-Chip, NOCS, 2018
  Mayank Parasar, N. Enright Jerger, P. Gratz, J. San Miguel, and T. Krishna, “SEEC: Stochastic Escape Express Channel,” under submission MICRO, 2020
Network Throughput Enhacement
  Mayank Parasar and T. Krishna, “Lightweight emulation of virtual channels using swaps,” in Proceedings of the 10th International Workshop on Network on Chip Architectures, NoCArc’17
Virtual Memory (Cache-TLB Co-design)
  Mayank Parasar, A. Bhattacharjee, and T. Krishna, “SEESAW: Using superpages to improve VIPT caches,” in 2018 ACM/IEEE 45th Annual International Symposium on Computer Architecture (ISCA), June 2018
Notes: In interest of time I will talk about Deadlock-freedom…
I would be happy to talk about my other work offline, after my presentation if any one is interested.

## Slide 4: Outline
Introduction
Prior Work in Deadlock Freedom
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 5: Why study NoCs now?
Interconnection Network takes the center stage

## Slide 6: Interconnection Networks

## Slide 7: Network on Chip
Control
Xbar
Router
West
East
South
North
Core
Buffers
Router micro-architecture
Source: Intel Teraflops, IEEE Micro 2007
Notes: After explaining about the importance of interconnection network let me show how interconnection network looks like in a chip.
It is a 4x4 Mesh
Here each tile has its own processor, has a private cache and a slice of Last level cache may be and connected with a router.
The green colored box represents the router.
Let us take a closer look to see how on-chip router looks like.
This is an input buffered Mesh router.
Here packets as they travel the network gets buffered at the input port before moving to next hop router, on its path to destination.
Control logic resolves any conflict if there are 2 or more packets which wants to go out from the same output port. It decides which packet will leave first.
After that packet traverse the X-bar, which connects input ports with output ports.
Packets now leave this router to go to the next hop router using these links. Packet will similarly, then get buffered at the next hop router

## Slide 8: Understanding Latency
Network Topology
Queuing Latency
Network Latency
Injection Rate

## Slide 9: Network Performance
Latency
Injection Rate (Packets/node/cycle)
Min latency given by topology
Min latency given by routing algorithm
Zero load latency
(topology+routing+flow control)
Throughput given by topology
Throughput given by routing
Throughput given by flow control
Saturation Throughput: the injection rate at which
latency ~3x(zero-load latency)
Network + Queueing Latency

## Slide 10: Outline
Introduction
  Deadlocks
Prior Work in Deadlock Freedom
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 11: Deadlock: Philosophy
Dining Philosopher Problem

## Slide 12: Challenge I: Routing Deadlock
9
5
10
6
5
9
6
10
Deadlock
5
Destination Router-5
Network
Network
Network
Network
Deadlock: Cyclic dependence between packets
Renders the forward progress of packets impossible
Correctness problem, can cause system failure
Notes: One of the fundamental problem each network must solve is that of deadlock.
Let me show how deadlocks can be manifested in the on-chip network.
this is an arbitrary network topology and we are focusing on these 4 routers where I will show the deadlock using animations.
Packets move in the network to reach their destination and the path is guided by the routing algorithm used in the network.
Packet can only move forward if there is free buffer present at the next hop router in their path towards destination.
Here num on the packet represent the destination router that packet wants to reach.
In doing so they may incur in cyclic dependency as shown here packet 5 cannot move down because the buffer is occupied by packet 6. Packet 6 cannot move right because the buffer is occupied by packet 10 and so on and so forth. This dependency comes back to packet 5. This cyclic dependency leads t a deadlock.
Rendering the forward movement of packet impossible,
And it is a correctness problem which can cause complete system failure.

## Slide 13: Challenge II: Protocol Deadlock
Interconnection Network
Interconnection Network can be visualized as queues of buffers transporting packets
Incoming Queue
Outgoing Queue
Finite Network Buffers
Notes: Second challenge is that of a protocol level deadlock.
To understand protocol level deadlock consider interconnection network to facilitate the movement of packets between nodes.
At a higher level, interconnection network can be considered as queues buffers for transporting packets from their source to destination
Little more animations
Priority inversion.
Protcol assumes that response will not get block…
[animation] two queues  one queue.. Remove left side of the slide
Left side it will not get blocked.. Right one it will get blocked.

## Slide 14: Challenge - II: Protocol deadlock
Protocols can deadlock even though network is deadlock-free
Cache 0
Directory
resp
resp
Responses should always be drained (“consumption assumption”)
req
req
req
req
req
req
req
req
Notes: Animate this slide
But protocols can also deadlock!!

## Slide 15: Challenge II: Protocol Deadlock
Cache
Directory
Request Packet
Response Packet
Finite Network Buffers
Cache
Directory
Dedicated queue (aka Virtual Network)
Injection queue
Dedicated Ejection queue
No virtual Network
Separate Virtual Network
Notes: Explain what is a virtual network
There can be different types of packets flowing in the network. If all types of packet share the same queue then
Higher priority packets may get blocked by lower priority packets as shown in the figure.
Here there is no cyclic dependency, but all the buffers of the network are exhausted by the request packet. This blocks the response packet forever to make forward progress. Response packet needs to reach to its destination for making forward progress of the whole system. This results in protocol level deadlock.
To resolve protocol deadlock separate queue for each message type is allocated, so that packets of one message type do not take up the buffers of other message types. These are called Virtual Network

## Slide 16: Buffers in Network
Routing Deadlock Avoidance
Protocol Deadlock Avoidance
For Performance
- not required
“Virtual Networks”
e.g.,
req and resp
HoL blocking
Buffer Turnaround
Multi-flit packets
Physical Channels
Virtual Channels
For Correctness
- required
- cannot be shared
VC0
VC1
VC2
VC4
.
.
.
- can be shared
Link
Router
Notes: This slide after introduction of virtual network to just show, how much buffering is typically present in the modern routers and our schemes free most of it, providing higher area and power benefits.

## Slide 17: Insight: Virtual Networks are underutilized!
MOESI
VNet-ID 
MESI
VNet-ID 
More coherence states to reduce network traversal
Router may need to support more virtual networks
Notes: These stacked bar-graphs shows the distribution of active and wasted power per virtual network…
Wasted power is XX times more than active power
And specifically more for MOESI protocol compared to MESI protocol.
------ Total number of cycles flits spends at all routers = ((Avg Latency per flit / Avg Hop Count) - 1) * Avg Hop Count * Total Flits Received
U = total number of cycles all the flits spend in all routers / (total sim cycle * total flit buffers) --- and then in this: -----active power should be 0.2*A; 0.6*A; 0.2*A wasted power should be (total power of 1 VNet) - 0.2*A; (total power of 1VNet) - 0.6*A; (total power of 1VNet) - 0.2*A---- A is U*(total power of 3 VNet)
right?

## Slide 18: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 19: Dealing with Deadlocks
Proactive
  Guarantees no deadlocks
Reactive
  Detect deadlock and correct

## Slide 20: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
    Routing Deadlock
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 21: Proactive Techniques
Routing
  Turn Restriction
Buffer Assignment
  Escape VCs
Flow Control
  Control traffic flow such that deadlock does not occur

## Slide 22: Proactive Solutions
Removing some turns can make the routing algorithm deadlock free
Pros
  Minimal Routing
Cons
  Only works for standard (fault-free), regular topologies
1. W. J. Dally and C. L. Seitz, “Deadlock-free message routing in multiprocessor interconnection networks,” IEEE Trans. Computer, May 1987.
2. Christopher J. Glass and Lionel M. Ni. The turn model for adaptive routing. ISCA, May 1992.
3. Daeho Seo, Akif Ali, Won-Taek Lim, Nauman Rafique, and Mithuna Thottenhodi. Near-optimal worst-case throughput routing for two-dimensional mesh networks. ISCA, June 2005.
4. Schroeder, Michael D., et al. “Autonet: a high-speed, self-configuring local area network using point-to-point links” IEEE Journal on Selected Areas in Communications, 1991.
5. Aisopos, Konstantinos, et al. "Ariadne: Agnostic reconfiguration in a disconnected network environment" 2011 PACT. IEEE, 2011.
XY Model
West-First
Turn Model
Negative-First
Turn Model
Notes: XY – Dimension order routing
WF/NFT: Turn model

## Slide 23: Channel Dependency Graph (CDG)
F
A
B
E
D
C
Function of both Topology and Routing Algorithm
Pros
  Works for any arbitrary topology
Cons
  Introduces non-minimal path and not scalable
Cycle

## Slide 24: Proactive Techniques
Routing
  Turn Model in a Mesh
Buffer Assignment
  Escape VCs
Flow Control
  Control traffic flow such that deadlock does not occur

## Slide 25: Proactive solution
[1] *José Duato. A new theory of deadlock-free adaptive routing in wormhole networks. IEEE Transactions on Parallel and Distributed Systems, December 1993.
Deadlock avoided if cycles eliminated in Channel Dependence Graph
It is possible for a CDG to have cycles and still be deadlock-free [1]
  As long as extended CDG is acyclic
  Known as the escape path or escape VC

## Slide 26: Example
Escape VC
West-first
Regular VCs
Deadlock-free
Acyclic path in extended CDG
Notes: Work on this slide
Because of the restriction and freedom both present simultaneously.. Network is deadlock free.
Uses a fine balance of restriction in packet movement and freedom to provide deadlock free network.

## Slide 27: Why escape VCs work?
At least one packet in the cycle has an option to take an acyclic route
  If allocation is fair, escape VCs guaranteed to show up eventually
If a message enters the escape network it can move back to the adaptive network, and vice versa, if minimal* routes
    *for non-minimal routes, message has to continue on escape VC once it gets in, without going back to the adaptive VCs

## Slide 28: Proactive Techniques
Routing
  Turn Model in a Mesh
Buffer Assignment
  Escape VCs
Flow Control
  Control traffic flow such that deadlock does not occur

## Slide 29: Bubble Flow Control
F
A
B
E
D
C
Ring Traversal Rule: traverse if one bubble free
BFC Injection Rule:
only inject if 2 bubbles free.
Occupied
Empty
V. Puente et al. The adaptive bubble router. Journal of Parallel and Distributed Computing, 2001.
L. Chen et al., “Critical Bubble Scheme: An Efficient Implementation of Globally Aware Network Flow Control,” IPDPS 2011

## Slide 30: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
    Routing Deadlock
    Protocol Deadlock
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 31: Proactive solution for Protocol Deadlock
Separate set of VCs (called as Virtual Network) for each message class at each input port
Bubble for each message class[1]
[1] Wang, Ruisheng, Lizhong Chen, and Timothy Mark Pinkston. "Bubble coloring: Avoiding routing-and protocol-induced deadlocks with minimal virtual channel requirement." Proceedings of the 27th international ACM conference on International conference on supercomputing. 2013.

## Slide 32: Challenges with Proactive Deadlock Freedom
Techniques | Full Path Diversity | No Deadlock Detect | No Misroute | No Extra Buffers | Routing deadlock free | Protocol deadlock free
Acyclic CDG (P) |  |  |  |  |  | 
Escape VC (P) |  |  |  |  |  | 
Bubble (P) |  |  |  |  |  | 
Deflection (P) |  |  |  |  |  | 
Qualitative Comparison of Deadlock Freedom Mechanisms. P: Proactive, R: Reactive. S: Subactive

## Slide 33: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
    Routing Deadlock
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 34: Insight: Deadlocks are rare!
blackscholes
bodytrack
canneal
fluidanimate
swaptions
Number of links removed 
0
1
2
4
8
16
20
24
1-vc
4-vc
1-vc
4-vc
1-vc
4-vc
1-vc
4-vc
1-vc
4-vc
Deadlock Probability
0%
20%
40%
60%
80%
100%
Requires certain ensemble of packets with a particular buffer dependency for the deadlock to occur
Notes: To quantify the likelihood of routing deadlocks in real application we performed the following experiments
With router configuration of 1-vc and 4-vc per virtual network
We took 8x8 Mesh and progressively removed links to see the likelihood of routing deadlock.
We did not observe the routing level deadlock where there were few faults, Only when the topology becomes fragmented by removing more number od links do we actually start observing the deadlocks.
This shows that deadlocks are rare, yet it is the correctness issue and must be resolved for the functioning of the network.

## Slide 35: Dealing with Deadlocks
Proactive
  Guarantee that the network will never deadlock
  Almost all modern networks use deadlock avoidance
Reactive
  Detect deadlock and correct

## Slide 36: SPIN: Synchronized Progress in Interconnection Networks
First spin
Second spin
Deadlock resolved
A. Ramrakhyani, P. V. Gratz, and T. Krishna, “Synchronized progress in interconnection networks (SPIN) : A new theory for deadlock freedom,” ISCA, 2018.
Notes: Fix these call-outs
Mention why you have chosen SPIN
“Very recent sate of the art” in reactive solutions

## Slide 37: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
    Routing Deadlock
    Protocol Deadlock
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 38: Reactive Solution for Protocol Deadlock
mDisha
  Disha recovery paths include end-point of the networks
  Extra buffers for recovery
  Detects and maps deadlock using probes at runtime
  Resolves deadlock using Disha recovery paths
Yong Ho Song, and T.M. Pinkston “A progressive approach to handling message-dependent deadlock in parallel computer systems”, IEEE Transactions on Parallel and Distributed Systems, 2003

## Slide 39: In Summary

## Slide 40: Routing Level Deadlock
A3
A4
A2
A8
A7
A6
Proactive Solution
NO
DEADLOCK
A1
A5
No Y to X turns in orange (escape) VC
All turns allowed in green VC
Reactive Solution
A3
A4
A2
A8
A7
A6
A1
A5
A4
A5
A3
A1
A8
A7
A2
A6
NO DEADLOCK
Synch via
probes

## Slide 41: Protocol level deadlock
B5
B4
B2
A3
A2
A6
A5
Proactive Solution
Replies are
not blocked
by requests
NO
DEADLOCK
B3
A4
A1
B6
B1
B2
A3
A2
B3
A4
A1
B6
B1
Synch via
probes
B5
B4
B2
A3
A2
B3
A4
A1
B6
B1
B5
B4
NO DEADLOCK
Reactive Solution

## Slide 42: Qualitative Comparison Table
Techniques | Full Path Diversity | No Deadlock Detect | No Misroute | No Extra Buffers | Routing deadlock free | Protocol deadlock free
Acyclic CDG (P) |  |  |  |  |  | 
Escape VC (P) |  |  |  |  |  | 
Bubble (P) |  |  |  |  |  | 
Deflection (P) |  |  |  |  |  | 
Deadlock Buffers (R) |  |  |  |  |  | 
Coordination (R) |  |  |  |  |  | 
Qualitative Comparison of Deadlock Freedom Mechanisms. P: Proactive, R: Reactive. S: Subactive

## Slide 43: Can we design our network…
Is free from routing and protocol level deadlocks?
Does not incur the cost of additional virtual channels irrespective of cache coherence protocol?
High performant?
  Full path diversity
  Minimal routing
  Topology agnostic
Has low area and power requirement at the same time readily implementable?
Notes: Can ignore this slide./\

## Slide 44: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 45: Subactive Approach: Thesis Statement
We show periodic coordinated packet movement is sufficient to resolve both routing and protocol deadlocks in any interconnection network

## Slide 46: The subactive approach
Proactive Deadlock Freedom
Reactive Deadlock Freedom
Subactive Deadlock Freedom
Prior Work
Contribution

## Slide 47: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 48
Mayank Parasar, Ankit Sinha and Tushar Krishna
Brownian Bubble Router*: Enabling Deadlock Freedom via Guaranteed Forward Progress
School of Electrical and Computer Engineering
Georgia Institute of Technology
mparasar3@gatech.edu
ankit.Sinha@gatech.edu
tushar@ece.gatech.edu
*Proceedings of the Twelfth IEEE/ACM International Symposium on Networks-on-Chip, NOCS, 2018

## Slide 49: BBR: Brownian Bubble Router [NOCS’18]
collision
What if we keep anyone lane always free to begin with?

## Slide 50: BBR: Walk-through
1
2
3
4
4
Deadlock!
C
C
C
C
Empty-VC tagged as ‘Brownian-Bubble’
Free-VC
Bubble Movement means reading out packet from its VC and writing it to empty VC marked as ‘Brownian Bubble’
Deadlock
Resolved!
BBR is free from Deadlock-detection complexity!
1
2
3

## Slide 51: Nuance about ‘Brownian Bubble’ movement
It moves randomly across input ports at a fixed rate
  BBR-‘k’, refers to the movement of bubble after ‘k’ cycles
BBR will always have one randomly initialized empty VC in the router
Bubble never goes into the injection-input port of the router
Notes: Reduce the text.

## Slide 52: BBR Microarchitecture
BBR moves packets from VCs of one port to VCs of another port
BBR bus for bubble movement
However, number of bubbles reduces the saturation throughput
Only 7% area and power overhead
Scalable to arbitrary topologies

## Slide 53: Qualitative Comparison Table
Techniques | Full Path Diversity | No Deadlock Detect | No Misroute | No Extra Buffers | Routing deadlock free | Protocol deadlock free
Acyclic CDG (P) |  |  |  |  |  | 
Escape VC (P) |  |  |  |  |  | 
Bubble (P) |  |  |  |  |  | 
Deflection (P) |  |  |  |  |  | 
Deadlock Buffers (R) |  |  |  |  |  | 
Coordination (R) |  |  |  |  |  | 
BBR (S) |  |  | * |  |  | 
Qualitative Comparison of Deadlock Freedom Mechanisms. P: Proactive, R: Reactive. S: Subactive
However, number of bubbles reduces the saturation throughput

## Slide 54
Mayank Parasar, and Tushar Krishna
BINDU*: Deadlock-Freedom with One Bubble in the Network
School of Electrical and Computer Engineering
Georgia Institute of Technology
mparasar3@gatech.edu
tushar@ece.gatech.edu
*Proceedings of the Thirteenth IEEE/ACM International Symposium on Networks-on-Chip, NOCS, 2019

## Slide 55: BBR: Brownian Bubble Router [NOCS’18]
collision
What if we keep anyone lane always free to begin with?

## Slide 56: BINDU: Bubble in Irregular Network for Deadlock Purging
What if we keep one lane always free in whole road-network to begin with?

## Slide 57: BINDU: Walk-through
Bindu Path
Bubble (Bindu)
Bindu Path: Any cyclic path that covers all the input ports of the all the routers in the topology

## Slide 58: BINDU: Walk-through
1
1
2
3
4
4
3
2
C
Deadlock resolved!
Bindu moves in a fixed path visiting all the input ports of the router
It naturally resolves any deadlock that comes in its way by displacing the packets
BINDU is free from Deadlock-detection complexity!
Empty-slot
Deadlock!

## Slide 59: BINDU Router Microarchitecture
Bindu path is confined to VC-0 of each inport (except injection port) of all the routers in the Network
However, single Bindu might take time to reach deadlock ring as network size increases
Notes: It has all the benefits of BBR in terms of scalability
But high performant because it has only one bubble/Bindu
Talk about limitation on latency

## Slide 60: Qualitative Comparison Table
Techniques | Full Path Diversity | No Deadlock Detect | No Misroute | No Extra Buffers | Routing deadlock free | Protocol deadlock free
Acyclic CDG (P) |  |  |  |  |  | 
Escape VC (P) |  |  |  |  |  | 
Bubble (P) |  |  |  |  |  | 
Deflection (P) |  |  |  |  |  | 
Deadlock Buffers (R) |  |  |  |  |  | 
Coordination (R) |  |  |  |  |  | 
BBR (S) |  |  | * |  |  | 
BINDU (S) |  |  |  |  |  | 
Qualitative Comparison of Deadlock Freedom Mechanisms. P: Proactive, R: Reactive. S: Subactive
However, single bubble present in the network may take time to visit and resolve the deadlock…

## Slide 61
Mayank Parasar, Natalie Enright Jerger, Paul V. Gratz, Joshua San Miguel and Tushar Krishna
SWAP*: Synchronized Weaving of Adjacent Packets for Network Deadlock Resolution
mparasar3@gatech.edu
*Proceedings of 52nd Annual IEEE/ACM International Symposium on Microarchitecture, MICRO-52, 2019
Notes: Hello I am Mayank Parasar from Georgia Tech.
This is a joint work with my advisor Dr. Tushar Krishna and my collaborators Dr. Natalie Jerger from Toronto, Dr. Paul Gratz from Texas A&M and Dr. Josh San Miguel from Wisconsin.
My talk is going to be about a novel technique of providing deadlock freedom by periodically swapping packets in the network.

## Slide 62: Traffic Deadlock
Deadlock
Notes: To understand SWAP let us visualize a traffic deadlock
Here each car is waiting on the next car to move in order to make forward progress.
This result in cyclic dependency leading to a traffic deadlock

## Slide 63: Swap to resolve traffic deadlock
Deadlock
Notes: Suppose with the help of chopper if we could in-place swap the position of cars then we can resolve traffic deadlock.

## Slide 64: Key Terms
‘swapFwd’ packet always makes forward progress
‘swapBack’ packet is interchanged with swapFwd packet in SWAP
‘Backtrack’ is an act where ‘swapBack’ yield its buffer for ‘swapFwd’ to make forward progress

## Slide 65: SWAP to resolve Network Deadlock
9
5
10
6
5
9
6
10
Deadlock
Network
Network
Network
Network
SWAP
swapFwd
swapBack
backtrack
Eject
Deadlock Resolved!
Notes: Similarly as shown before circular dependency of packets can result in traffic deadlock.
If we can in-place swap the packets then we can resolve routing deadlock
Here the packet which makes forward progress is called as swap-forward packet
And the packet which backtrack, by yielding its buffer to be occupied by swap forward packet is called as swapBack packet.
Now packet for destination router 5 has reached its router and will be ejected out from the network.

## Slide 66: SWAP
Notes: Reduce the time spend here

## Slide 67: SWAP: Router microarchitecture
Notes: Skim though it…
In interest of time I am skipping it.. can chat about it later

## Slide 68: Qualitative Comparison Table
Techniques | Full Path Diversity | No Deadlock Detect | No Misroute | No Extra Buffers | Routing deadlock free | Protocol deadlock free
Acyclic CDG (P) |  |  |  |  |  | 
Escape VC (P) |  |  |  |  |  | 
Bubble (P) |  |  |  |  |  | 
Deflection (P) |  |  |  |  |  | 
Deadlock Buffers (R) |  |  |  |  |  | 
Coordination (R) |  |  |  |  |  | 
BBR (S) |  |  | * |  |  | 
BINDU (S) |  |  |  |  |  | 
SWAP (S) |  |  |  |  |  | 
Qualitative Comparison of Deadlock Freedom Mechanisms. P: Proactive, R: Reactive. S: Subactive
SWAP can provide routing and protocol level deadlock freedom, however there can be misrouting…

## Slide 69
Mayank Parasar, Hossein Farrokhbakht, Natalie Enright Jerger, Paul V. Gratz, Tushar Krishna, Joshua San Miguel
DRAIN*: Deadlock Removal for Arbitrary Irregular Networks
mparasar3@gatech.edu
*Proceedings of 26th IEEE International Symposium on High-Performance Computer Architecture (HPCA) 2020
Notes: Good morning!
I am Mayank Parasar from Georgia Tech. Today I will talk about a novel technique called DRAIN, which provides deadlock freedom in any network topology by periodically moving packets in the network.

## Slide 70: Traffic Deadlock
Oblivious Movement
Deadlock
Notes: To understand DRAIN, let us consider the traffic deadlock as shown in the figure… Here each car is waiting on the next car to move in order to make forward progress, resulting in traffic deadlock.
If we provide oblivious periodic movement to all the cars in this road network, then this will flush out any deadlock as shown in the animation.
All cars are unblocked and will reach to their destination.
The same idea is used in DRAIN to resolve deadlock, if consider cars as packets and roads as the links in the network

## Slide 71: Virtual ring (DRAIN-Path) over topology
Every link is spun exactly once, simultaneously
Oblivious packet movement over the virtual ring
0
1
2
3
5
4
7
6
0
1
2
3
4
5
6
7
8
Mesh
Irregular
Notes: DRAIN forms a virtual ring over the topology.. As I am showing it for 3x3 Mesh. This is also applicable to other irregular topologies.
The virtual ring is formed such that each link is spun/covered only once, and all the links are covered. This makes sure that there is no collision of packets when spun over this virtual ring
Oblivious packet movement over this virtual ring makes sure that if there is any deadlock in the network, it is flushed out.

## Slide 72: DRAIN to resolve Routing Deadlock
Pkt destination
Pkt Route
Deadlock
Deadlock
Irregular 3x3 Mesh topology
DRAIN Path
Notes: This figure shows how DRAIN resolve routing deadlock in a irregular 3x3 Mesh.

## Slide 73: DRAIN to resolve Protocol Deadlock
Response Pkt
Request Pkt
Irregular Mesh
Response Packet is unblocked and reaches its destination
Response Packet Blocked
Protocol Deadlock!
Notes: This figure shows how DRAIN resolve protocol deadlock in same irregular 3x3 Mesh.

## Slide 74: DRAIN: Router microarchitecture
Turn-Table
Epoch register
Credit freeze
Full-Drain Counter
DRAIN is completely decentralized and requires relatively low hardware overhead
Notes: Fairly low level detail
Decentrallized, relatively low hardware
Keep the image
Don’t drag through
I encourage to read the paper.. I can answer more details

## Slide 75: Qualitative Comparison Table
Techniques | Full Path Diversity | No Deadlock Detect | No Misroute | No Extra Buffers | Routing deadlock free | Protocol deadlock free
Acyclic CDG (P) |  |  |  |  |  | 
Escape VC (P) |  |  |  |  |  | 
Bubble (P) |  |  |  |  |  | 
Deflection (P) |  |  |  |  |  | 
Deadlock Buffers (R) |  |  |  |  |  | 
Coordination (R) |  |  |  |  |  | 
BBR (S) |  |  | * |  |  | 
BINDU (S) |  |  |  |  |  | 
SWAP (S) |  |  |  |  |  | 
DRAIN (S) |  |  |  |  |  | 
Qualitative Comparison of Deadlock Freedom Mechanisms. P: Proactive, R: Reactive. S: Subactive
DRAIN can provide routing and protocol level deadlock freedom, however there can be misrouting…

## Slide 76: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion

## Slide 77
Mayank Parasar, Natalie Enright Jerger, Paul V. Gratz, Joshua San Miguel and Tushar Krishna
SEEC: Stochastic Escape Express Channel
mparasar3@gatech.edu
Notes: Good morning!
I am Mayank Parasar from Georgia Tech. Today I will talk about a novel technique called DRAIN, which provides deadlock freedom in any network topology by periodically moving packets in the network.

## Slide 78: SEEC: Deadlock Analogy
Deadlock
Destination
Notes: To understand SWAP let us visualize a traffic deadlock
Here each car is waiting on the next car to move in order to make forward progress.
This result in cyclic dependency leading to a traffic deadlock
Give example of Amazon-Prime which delivers product using drones..

## Slide 79: SEEC: Performance Analogy
Destination-1
Destination-2
Destination-3
2
1
3
Notes: This is to motivate the buffer turn around time.

## Slide 80: SEEC: Performance Analogy
Destination-1
Destination-2
Destination-3
1
3
2

## Slide 81: SEEC: Walk-through (Correctness)
9
5
10
6
2
3
1
13
14
15
11
7
0
4
8
12
1
7
14
8
Static-Round robin order of FF ejection of packets
My turn
All packets travel minimally
Seeker
My turn
My turn
Seeker
Deadlock
S
E
W
N
Seeker Path
Seeker
Search Router-9 onwards
Search Router-5 onwards
Search Router-10 onwards
Free Slot
1
NIC
Notes: Each router when done with its seeker passing, signals the neighboring router of its turn to send the seeker.. This is done in a round-robin fashion over the network topology.

## Slide 82: Definitions
Free Flow (FF)
FF packet
Seeker
Seeker Path
Lookahead
mSEEC
Notes: Free Flow (FF)
  Flow control where packets are not buffered and move forward without need for credit
Seeker
  Token sent out by the destination N IC after reserving an ejection VC within a specific message class.
Seeker Path
  A side-band network connecting all routers in the network over which the seeker visits all routers, and comes back to its initiator in case it does not find a packet.
FF packet
  This packet is chosen by the seeker and traverses to its destination over a minimal path using FF.
Lookahead
  Signaling mechanism to support FF packet, so that next router prioritized incoming FF packet
mSEEC

## Slide 83: Novel Flow Control: FF Control
FF: Free Flow Control
FF packet gets prioritized over the buffered packets
Packet becomes FF by sending a lookahead signal
lookahead signal sets the appropriate mux at downstream router
FF packet traverse the network from link to link
SEEC proposes co-existence of FF packets and buffered packets

## Slide 84: SEEC: Router Microarchitecture

## Slide 85: SEEC: Walk-through (Performance)
9
5
10
6
2
3
1
13
14
15
11
7
0
4
8
12
0
0
0
0
1
0
0
0
Congestion
Seeker
Free Slot
1
NIC
My Turn
0
3
SEEC helps packets to bypass congestion in the network

## Slide 86: SEEC: Nuances
All packets, buffered and FF, follow minimal routing using network full path diversity
Seeker Path:
  Any pre-defined path that visits all router in a cyclic manner
  Seeker can follow minimal path to start the search from
Packets are upgraded to follow FF till ejection
FF packet path is decided by the routing algorithm

## Slide 87: SEEC: Mathematical upper bound
For any irregular network topology:
  Assume diameter is D
  Assume it takes on an average ‘k’ cycles at the ejection port
  Number of nodes in the network is ‘N’
  Let the average network router-radix of the router is ‘r’
The maximum time it takes for a deadlock to persist
  Deadlock involves at least 4 routers
  [{r*(N-4)*2*D*k} + (D+k)] cycles

## Slide 88: Normalized Area and Static Power
Chart: 
| Area | Power
Escape VCs | 1 | 1
SPIN | 0.86277 | 0.85627
SWAP | 0.82168 | 0.82333
DRAIN | 0.41813 | 0.35775
SEEC | 0.39822 | 0.34071
~70% Lower Static Power
~65% Lower Static Area
Notes: Major Area/power savings comes from lower buffer overhead.

## Slide 89: Multi-SEEC (mSEEC)
Motivation
  Path Diversity: Multiple ways of reaching a node
  Link arrangements in topology provide path diversity
Features
  Creates multiple FF packets to traverse simultaneously
Requirement
  Multiple FF packets traverse minimally wo overlapping paths
Implementation
  mSEEC divides the topology into independent regions

## Slide 90: mSEEC: Walk Through
A
B
C
D
E
F
G
H
I
0
1
2
Partition
Group-0
A
B
C
D
E
F
G
H
I
0
1
2
A
B
C
D
E
F
G
H
I
0
1
2
When Phase-0 finishes:
  each node in group-0 has searched entire topology
Phase-1 starts

## Slide 91: mSEEC: Walk Through
A
B
C
D
E
F
G
H
I
0
1
2
Partition
Group-1
A
B
C
D
E
F
G
H
I
0
1
2
A
B
C
D
E
F
G
H
I
0
1
2
When Phase-1 finishes:
  each node in group-1 has searched entire topology
Phase-2 starts and so on…

## Slide 92: mSEEC
mSEEC provides higher throughput than SEEC
mSEEC achieves this by making multiple FF packets
Each group is a ‘row’ in the Mesh
Each partition is a ‘column’ in the Mesh
As Mesh size increases the path diversity increases
As Mesh size increases more packets can become FF
mSEEC is truly scalable version of SEEC

## Slide 93: Deadlock Freedom Proof
The ejection port at NIC has separate Virtual Networks
The response packet can cause a protocol deadlock, if stuck in network
SEEC/mSEEC is protocol deadlock free as NIC will eject response packet by sending seeker as it gets a free-slot
SEEC/mSEEC is routing deadlock free as all the input ports get chance to send packets via FF flow control
SEEC/mSEEC is livelock free as there is no misrouting

## Slide 94: Qualitative Comparison Table
Techniques | Full Path Diversity | No Deadlock Detect | No Misroute | No Extra Buffers | Routing deadlock free | Protocol deadlock free
Acyclic CDG (P) |  |  |  |  |  | 
Escape VC (P) |  |  |  |  |  | 
Bubble (P) |  |  |  |  |  | 
Deflection (P) |  |  |  |  |  | 
Deadlock Buffers (R) |  |  |  |  |  | 
Coordination (R) |  |  |  |  |  | 
BBR (S) |  |  | * |  |  | 
BINDU (S) |  |  |  |  |  | 
SWAP (S) |  |  |  |  |  | 
DRAIN (S) |  |  |  |  |  | 
SEEC/mSEEC (S) |  |  |  |  |  | 
Qualitative Comparison of Deadlock Freedom Mechanisms. P: Proactive, R: Reactive. S: Subactive

## Slide 95: Results: SEEC-Performance Topology Sweep
Chart: 4x4 Mesh Shuffle
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5 | 0.52 | 0.54 | 0.56000000000000005 | 0.57999999999999996 | 0.6 | 0.62
XY | 9.0073 | 9.0117 | 9.0159 | 9.0193 | 9.0265 | 9.0346 | 9.0443 | 9.0551 | 9.0636 | 9.077 | 9.0947 | 9.1146 | 9.1365 | 9.1631 | 9.1943 | 9.2318 | 9.2786 | 9.3376 | 9.4169 | 9.5248 | 9.6841 | 9.9546 | 10.483 | 12.0593 | 69.818 | 975.3691 | 1798.2586 | 2539.7275 | 3204.4234 | 3799.5834 | 4324.7271
WestFirst | 9.0079 | 9.0137 | 9.0197 | 9.0242 | 9.0322 | 9.0413 | 9.0531 | 9.0672 | 9.0766 | 9.092 | 9.1115 | 9.1329 | 9.1587 | 9.1902 | 9.2237 | 9.2655 | 9.3191 | 9.3778 | 9.4705 | 9.5893 | 9.7777 | 10.1506 | 11.0383 | 59.2888 | 324.9363 | 830.6292 | 1257.7241 | 1628.678 | 2036.7977 | 2376.0309 | 2919.3188
EscapeVC | 9.0088 | 9.0156 | 9.0251 | 9.0301 | 9.0391 | 9.0512 | 9.0626 | 9.0789 | 9.0893 | 9.1062 | 9.1282 | 9.1518 | 9.1776 | 9.2073 | 9.243 | 9.285 | 9.331 | 9.3825 | 9.4513 | 9.5414 | 9.6406 | 9.8043 | 10.0612 | 10.4795 | 11.7632 | 167.4862 | 384.1705 | 773.2326 | 1328.6097 | 1868.8782 | 2541.8906
SPIN | 9.0073 | 9.0117 | 9.0159 | 9.0193 | 9.0265 | 9.0346 | 9.0443 | 9.0551 | 9.0637 | 9.0771 | 9.0948 | 9.1147 | 9.1366 | 9.1633 | 9.1947 | 9.232 | 9.2793 | 9.3385 | 9.4188 | 9.5289 | 9.6906 | 9.9701 | 10.5267 | 12.3112 | 133.5509 | 985.902 | 1682.2878 | 2250.1111 | 2697.8692 | 3055.4757 | 3453.0847
SWAP | 9.0097 | 9.0171 | 9.0242 | 9.0298 | 9.0412 | 9.0511 | 9.0649 | 9.0794 | 9.0902 | 9.1081 | 9.1295 | 9.1535 | 9.1793 | 9.2062 | 9.2364 | 9.2747 | 9.313 | 9.3551 | 9.4051 | 9.4635 | 9.5308 | 9.6084 | 9.7127 | 9.8418 | 10.0237 | 10.3427 | 11.0094 | 29.4089 | 330.8975 | 618.5831 | 857.483
DRAIN | 9.0041 | 9.0452 | 9.0531 | 9.0591 | 9.0685 | 9.0784 | 9.0887 | 9.1019 | 9.1128 | 9.1282 | 9.1458 | 9.169 | 9.1914 | 9.2146 | 9.2438 | 9.2746 | 9.3115 | 9.3496 | 9.3958 | 9.4439 | 9.5074 | 9.568 | 9.6626 | 9.772 | 9.9306 | 10.1873 | 10.8259 | 50.9292 | 106.0356 | 192.0124 | 200.2222
SEEC | 9.0094 | 9.0159 | 9.0226 | 9.0287 | 9.0391 | 9.0496 | 9.0625 | 9.0756 | 9.0872 | 9.1036 | 9.1222 | 9.1449 | 9.1674 | 9.1938 | 9.2219 | 9.2548 | 9.2902 | 9.3261 | 9.3691 | 9.4202 | 9.479 | 9.5466 | 9.63 | 9.7429 | 9.8968 | 10.1308 | 10.6161 | 13.2583 | 209.0278 | 484.0463 | 705.0305
mSEEC | 9.0064 | 9.0102 | 9.0142 | 9.0187 | 9.0248 | 9.0327 | 9.0421 | 9.0531 | 9.0608 | 9.0732 | 9.0882 | 9.1056 | 9.1246 | 9.1405 | 9.1635 | 9.1885 | 9.2135 | 9.2409 | 9.2735 | 9.3082 | 9.347 | 9.3952 | 9.4468 | 9.5156 | 9.598 | 9.6945 | 9.8242 | 10.0256 | 10.3918 | 11.8263 | 89.9882
Chart: 8x8 Mesh Shuffle
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46
XY | 13.0555 | 13.0904 | 13.1326 | 13.1832 | 13.2529 | 13.3445 | 13.4776 | 13.6767 | 14.051 | 15.005 | 24.3331 | 2344.5924 | 4387.8568 | 6009.6388 | 7149.3184 | 8187.375
WestFirst | 13.0569 | 13.0968 | 13.1427 | 13.1984 | 13.2751 | 13.3746 | 13.5233 | 13.7657 | 14.463 | 270.7534 | 3369.2477 | 4936.4574 | 5578.4071 | 6248.9391 | 6749.3591 | 7318.3032
EscapeVC | 13.0594 | 13.1003 | 13.1468 | 13.2036 | 13.2798 | 13.3764 | 13.5083 | 13.6964 | 3253.6677 | 6170.2839 | 7203.8125 | 8383.5611 | 8847.5037 | 9478.3958 | 10157.5422 | 10361.371
SPIN | 13.0558 | 13.0907 | 13.1338 | 13.1855 | 13.2577 | 13.3535 | 13.4921 | 13.7072 | 14.143 | 17.132 | 571.8515 | 1677.1668 | 2783.9625 | 4130.6942 | 4838.5402 | 5528.292
DRAIN | 13.1091 | 13.1486 | 13.1979 | 13.2536 | 13.324 | 13.4066 | 13.51 | 13.6256 | 13.7715 | 13.948 | 14.1642 | 14.4488 | 14.8437 | 15.5409 | 17.6302 | 257.0386 | 623.0671 | 828.7812 | 977.2559 | 1063.6576 | 1077.9888 | 1092.9766 | 1156.2063 | 1211.0887 | 1299.6186
SWAP | 13.0609 | 13.1031 | 13.1536 | 13.2118 | 13.2858 | 13.3743 | 13.4859 | 13.611 | 13.7757 | 13.9621 | 14.1993 | 14.5106 | 14.9136 | 15.5272 | 16.6764 | 157.4206
SEEC | 13.0605 | 13.1033 | 13.152 | 13.2073 | 13.2783 | 13.3635 | 13.4659 | 13.5809 | 13.7306 | 13.8989 | 14.1105 | 14.3855 | 14.7445 | 15.2674 | 16.2619 | 198.5061 | 1773.2761 | 3126.1223 | 4752.9684
mSEEC | 13.043 | 13.0658 | 13.0945 | 13.1278 | 13.1724 | 13.2257 | 13.2889 | 13.3556 | 13.439 | 13.5294 | 13.6343 | 13.752 | 13.8868 | 14.0473 | 14.2221 | 14.4289 | 14.675 | 14.969 | 15.3324 | 15.8099 | 16.513 | 17.8262 | 64.4376 | 755.9479 | 1752.0984
Chart: 16x16 Mesh Shuffle
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
XY | 21.1079 | 21.2553 | 21.4886 | 21.9718 | 39.0045 | 3665.7192 | 3892.7815 | 4842.7744 | 4544.0189 | 6252.2716
WestFirst | 21.1381 | 21.3358 | 21.6587 | 23.8373 | 2434.7214 | 4649.9591 | 4704.7817 | 5384.3543 | 5103.5599 | 6353.5247
EscapeVC | 21.1455 | 21.358 | 21.6998 | 651.6404 | 6778.2685 | 5975.6013 | 7752.6127 | 7188.3503 | 8377.4474 | 8165.1975
SPIN | 21.1083 | 21.2582 | 21.499 | 21.971 | 121.4896 | 2892.7109 | 4318.4847 | 5558.4027 | 6853.3961 | 7351.6657
SWAP | 21.1693 | 21.4019 | 21.7432 | 22.2327 | 22.9878 | 24.2157 | 1598.1542 | 4062.4437 | 4158.3274 | 4537.8115
DRAIN | 21.2247 | 21.4471 | 21.7639 | 22.2082 | 22.8546 | 23.885 | 27.7587 | 5053.6317 | 5593.5508 | 5202.0516 | 5219.5427
SEEC | 21.1661 | 21.3916 | 21.7125 | 22.1619 | 22.8279 | 23.8961 | 26.4163 | 1999.086 | 1990.0457 | 1956.4885 | 2084.377
mSEEC | 21.087 | 21.2145 | 21.3903 | 21.6067 | 21.8774 | 22.1946 | 22.5753 | 23.0292 | 23.61 | 24.6179 | 18329.7871
11% over subactive techniques
25% over prior work
30% over subactive techniques
40% over prior work
40% over subactive techniques
57% over prior work

## Slide 96: Results: SEEC-Throughput Enhancement
Chart: Saturation Throughput
| 4x4 Mesh | 8x8 Mesh | 16x16 Mesh
XY | 0.12 | 0.08 | 0.04
SWAP-XY | 0.12 | 0.08 | 0.04
SEEC-XY | 0.14 | 0.08 | 0.04
Uniform Random
XY Routing
Chart: Saturation Throughput
| 4x4 Mesh | 8x8 Mesh | 16x16 Mesh
WF | 0.12 | 0.06 | 0.02
SWAP-WF | 0.12 | 0.06 | 0.02
SEEC-WF | 0.14 | 0.06 | 0.02
Uniform Random
West First Routing
16% throughput improvement in 4x4 Mesh

## Slide 97: Results: SEEC-%age of FF packets
Chart: Uniform Random 8x8 Mesh VC-2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
Bufferless pkt | 2.2889 | 5.0467 | 7.921 | 10.3565 | 11.8548 | 45.5702 | 95.8318 | 96.6899 | 96.1857 | 96.821 | 96.8652
Chart: Transpose 8x8 Mesh VC-2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
Bufferless pkt | 1.5625 | 3.72 | 6.2292 | 8.5301 | 10.5557 | 11.5596 | 11.1537 | 10.3842 | 9.8012 | 9.3152 | 8.9143
Chart: Bit Complement 8x8 Mesh VC-2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22
Bufferless pkt | 7.5231 | 17.32 | 98.8496 | 99.5658 | 99.8472 | 99.8771 | 99.8452 | 99.939 | 99.8452 | 99.928 | 99.9241

## Slide 98: Results: SEEC-Network Latency breakdown
Chart: Uniform Random 8x8 Mesh VC-2
| Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12
Buffered | 13.5289 | 9.3383 | 13.5506 | 9.2854 | 13.6494 | 9.376 | 13.8623 | 9.5084 | 14.2783 | 9.9191 | 79.1606 | 140.2012
Bufferless | 0 | 8.0814 | 0 | 8.3567 | 0 | 8.46 | 0 | 8.5756 | 0 | 8.6957 | 0 | 11.6904
Chart: Transpose 8x8 Mesh VC-2
| Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | Reg | FF | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14 | 0.16 | 0.18 | 0.2 | 0.22
Buffered | 13.4985 | 8.7134 | 13.5 | 8.9645 | 13.533 | 9.1119 | 13.6167 | 9.2506 | 13.851 | 9.5884 | 14.5134 | 10.2677 | 18.3957 | 14.584 | 22.4618 | 21.5759 | 22.7639 | 22.662 | 22.916 | 23.2239 | 22.7319 | 23.1842
Bufferless | 0 | 10.8642 | 0 | 10.7054 | 0 | 10.7029 | 0 | 10.8344 | 0 | 11.0355 | 0 | 11.5925 | 0 | 15.3489 | 0 | 17.1645 | 0 | 16.5308 | 0 | 16.1244 | 0 | 15.9175

## Slide 99: Results: Subactive Techniques
Chart: Bit Complement 8x8 Mesh VC=2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34
BBR | 22.4528 | 640.5844 | 663.2657 | 637.6628 | 462.9275 | 600.8848 | 604.0454 | 582.6279 | 587.8447 | 574.8433 | 586.8418 | 518.9514 | 580.2018 | 550.0117 | 574.8601 | 549.4612 | 532.0994
BINDU | 21.4983 | 22.9027 | 728.6863 | 261.47 | 283.6297 | 239.0941 | 602.0095 | 597.038 | 220.9842 | 641.6991 | 469.3507 | 332.6237 | 710.8542 | 389.3648 | 693.4012 | 234.9377 | 585.1371
DRAIN | 21.2958 | 21.9518 | 85.464 | 33515.5054 | 36692.763 | 34247.7289 | 32969.2355 | 33525.5456 | 32644.2589 | 33020.6434 | 34469.4015 | 34977.8332 | 36490.4751 | 34648.8588 | 36686.3535 | 38061.4223 | 34256.7703
SWAP | 21.4773 | 22.9564 | 33746.6242 | 40146.0406 | 40727.0959 | 42372.8007 | 44712.1298 | 44975.8492 | 44025.2371 | 47184.584 | 47446.4747 | 46388.3488 | 47088.9337 | 48059.3598 | 48123.1132 | 47196.7391 | 47993.5431
SEEC | 21.2764 | 21.9302 | 23.326 | 27547.6071 | 33249.7922 | 35472.9673 | 38714.9651 | 39896.697 | 41388.9331 | 42115.4253 | 43064.8846 | 43648.2171 | 43668.2254 | 44360.8639 | 44860.515 | 45037.5642 | 45392.3418
mSEEC | 21.2691 | 21.8018 | 22.4385 | 23.1177 | 23.8476 | 24.6655 | 25.7458 | 27.7884 | 13286.691 | 16812.2474 | 19984.6685 | 22569.8998 | 24806.4506 | 26516.5025 | 28386.6067 | 29515.4552 | 30769.9256
Chart: Transpose 8x8 Mesh VC=2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48 | 0.5 | 0.52 | 0.54 | 0.56000000000000005 | 0.57999999999999996 | 0.6 | 0.62 | 0.64 | 0.66 | 0.68 | 0.7
BBR | 15.9217 | 16.3999 | 16.9714 | 17.7934 | 19.4091 | 126.6818 | 877.9103 | 779.7109 | 820.0087 | 837.9207 | 843.0287 | 837.3516 | 826.7579 | 814.2371 | 804.2334 | 798.7732 | 793.907 | 788.1835 | 786.5536 | 780.7381 | 766.0131 | 755.1669 | 741.1364 | 729.7806 | 722.2595 | 712.1193 | 704.5235 | 699.3458 | 690.6539 | 684.6211 | 678.202 | 675.4782 | 664.5663 | 665.5888 | 657.1621
BINDU | 15.6134 | 15.8044 | 16.0639 | 16.4391 | 17.0228 | 18.1931 | 21.9167 | 148.75 | 479.2597 | 848.5371 | 758.2603 | 716.8537 | 727.14 | 739.3134 | 755.6733 | 765.2637 | 764.4449 | 766.4062 | 765.5099 | 768.8056 | 776.8089 | 780.5272 | 779.3986 | 770.2139 | 760.3335 | 748.1296 | 740.453 | 732.4474 | 723.7913 | 717.0035 | 708.7559 | 703.1825 | 697.0267 | 692.865 | 686.4777
DRAIN | 15.6491 | 15.7747 | 15.9491 | 16.1922 | 16.5827 | 17.3446 | 20.2811 | 697.4648 | 1406.6828 | 1928.1332 | 2411.5861 | 2908.6597 | 3134.9599 | 3389.3409 | 3566.8285 | 3638.9103 | 3725.4782 | 3793.4147 | 3829.3382 | 3948.2593 | 4347.6867 | 4432.2719 | 4470.7359 | 4486.8644 | 4501.3572 | 4514.6975 | 4522.433 | 4527.2057 | 4531.9939 | 4540.0101 | 4540.4332 | 4547.2904 | 4549.1536 | 4553.1139 | 4557.2806
SWAP | 15.6071 | 15.7849 | 16.0593 | 16.4645 | 17.1039 | 18.3055 | 22.0823 | 1106.1126 | 2721.4371 | 4584.6542 | 6235.4717 | 8104.943 | 9862.2823 | 11467.4908 | 13005.6201 | 14309.2156 | 15546.0769 | 16571.4341 | 17476.6181 | 18329.3126 | 19767.3612 | 21152.6855 | 22418.6733 | 23563.4656 | 24607.4217 | 25577.3229 | 26493.9087 | 27329.2667 | 28110.4685 | 28825.3544 | 29505.4782 | 30134.045 | 30733.8365 | 31294.8268 | 31857.7866
SEEC | 15.5814 | 15.7021 | 15.8749 | 16.0975 | 16.4237 | 16.9467 | 17.9345 | 20.7378 | 823.5735 | 2445.9671 | 4548.5479 | 6155.8812 | 7637.1706 | 9421.385 | 10951.4891 | 12402.5567 | 13619.6463 | 14910.3634 | 16048.2802 | 17060.8319 | 18583.2317 | 20009.6525 | 21321.1444 | 22507.0161 | 23618.5823 | 24624.7837 | 25567.0922 | 26439.366 | 27231.8429 | 27986.045 | 28691.6854 | 29355.1715 | 29987.7801 | 30574.462 | 31127.4333
mSEEC | 15.5803 | 15.6987 | 15.8593 | 16.0362 | 16.2517 | 16.5037 | 16.7937 | 17.1239 | 17.5061 | 17.9886 | 18.6103 | 19.5753 | 21.406 | 36.0802 | 898.282 | 2272.0299 | 3842.1176 | 5667.1212 | 7502.3504 | 9148.9749 | 11048.9892 | 12826.0264 | 14453.3476 | 15922.0157 | 17286.9949 | 18555.3267 | 19713.3387 | 20793.4563 | 21803.1469 | 22733.1789 | 23608.8054 | 24425.0569 | 25206.9967 | 25931.5512 | 26617.4601
Chart: Uniform Random 8x8 Mesh VC=2
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4
BBR | 15.9429 | 16.4113 | 17.1044 | 17.9977 | 19.9062 | 484.3102 | 505.0849 | 491.1155 | 496.9902 | 473.6292 | 475.9132 | 519.8829 | 528.1627 | 460.0706 | 472.3287 | 506.6123 | 481.2528 | 445.5004 | 472.341 | 473.4933
BINDU | 15.6173 | 15.7951 | 16.1741 | 16.623 | 17.3659 | 18.674 | 103.1612 | 127.0641 | 124.04 | 143.5983 | 221.9715 | 240.5194 | 154.149 | 356.4829 | 158.8871 | 295.6462 | 193.7816 | 219.9823 | 199.4793 | 307.54
DRAIN | 15.6653 | 15.7827 | 15.9931 | 16.3122 | 16.791 | 17.5758 | 2160.6061 | 37973.2451 | 39464.2115 | 39720.1249 | 42054.685 | 39312.0802 | 41648.8612 | 40557.7296 | 42647.4724 | 43024.2053 | 40377.0225 | 42078.6559 | 41756.0966 | 41059.9273
SWAP | 15.6296 | 15.8228 | 16.1512 | 16.6446 | 17.3744 | 18.6301 | 22262.2322 | 39891.3744 | 41560.8345 | 43117.6786 | 44527.6272 | 43182.253 | 43921.889 | 43931.1717 | 44220.944 | 46747.455 | 43196.0839 | 45633.444 | 45760.9852 | 45790.3762
SEEC | 15.5984 | 15.7198 | 15.9196 | 16.2105 | 16.6395 | 17.2791 | 18.524 | 36873.4951 | 42438.7098 | 43622.2835 | 44719.6244 | 44944.6621 | 44760.715 | 45896.1311 | 46098.297 | 45601.6594 | 46789.1409 | 46593.6131 | 46600.3914 | 46936.2476
mSEEC | 15.5977 | 15.7152 | 15.8948 | 16.1142 | 16.3701 | 16.6326 | 16.9497 | 17.3149 | 17.731 | 18.2714 | 18.9733 | 20.1198 | 22.6315 | 3508.3067 | 7040.6321 | 9884.5694 | 12173.4371 | 14287.5092 | 16269.5302 | 17876.7569
We observe following performance order (subactive techniques only) : BBR < BINDU ≈ DRAIN ≈ SWAP < SEEC < mSEEC

## Slide 100: Results: Full System Simulation
Chart: MOESI-hammer
| Bodytrack | canneal | FFT | Fmm | Lu_cb | Ocean_cp | Volrend | Average
EscapeVC | 29.2979 | 29.4994 | 43.6821 | 32.7665 | 27.9085 | 79.6328 | 27.0051 | 38.5418
SPIN | 26.3546 | 25.0486 | 32.7634 | 29.0533 | 25.3781 | 46.6958 | 24.702 | 29.9994
BBR | 34.9794 | 41.1316 | 59.3491 | 43.5212 | 33.1161 | 76.1526 | 30.3497 | 45.5143
BINDU | 30.933 | 32.0144 | 64.3009 | 35.7084 | 28.5212 | 63.8707 | 27.34 | 40.3841
SWAP | 27.6642 | 27.5465 | 40.8853 | 32.1812 | 26.3764 | 52.7619 | 25.5965 | 33.2874
DRAIN | 30.9348 | 26.2545 | 46.4669 | 35.1087 | 27.7605 | 59.3914 | 26.3159 | 36.0333
SEEC | 25.5776 | 26.5732 | 35.5779 | 28.9017 | 24.9353 | 42.08 | 24.2754 | 29.703
mSEEC | 22.8178 | 24.4046 | 27.2993 | 25.4785 | 23.2531 | 30.0848 | 22.7991 | 25.1624
mSEEC provides 37% lower packet latency compared to baseline Escape VC in 4x4 Mesh
SEEC/mSEEC use 1/6th of total buffer area

## Slide 101: Result: Max Packet Latency
Chart: Max Packet Latency
| Canneal | FMM | Lu_cb | Ocean_cp | Radix | Average
XY | 1493 | 1703 | 787 | 4490 | 1481 | 1990.8
WF | 1416 | 1413 | 674 | 4160 | 1302 | 1793
Escape-VC | 637 | 1354 | 523 | 2831 | 2865 | 1642
SPIN | 399 | 6336 | 1280 | 33280 | 3456 | 8950.2
SWAP | 858 | 1498 | 622 | 5688 | 1112 | 1955.6
DRAIN | 192954 | 327414 | 86451 | 1728 | 233976 | 168504.6
SEEC | 212 | 665 | 171 | 4315 | 306 | 1133.8
mSEEC | 52 | 56 | 37 | 94 | 50 | 57.8
mSEEC has the lowest max packet latency

## Slide 102: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 103
Mayank Parasar, Natalie Enright Jerger, Paul V. Gratz, Joshua San Miguel and Tushar Krishna
DRAGON: Deadlock Recognizing Topology Agnostic Network
mparasar3@gatech.edu
Notes: Good morning!
I am Mayank Parasar from Georgia Tech. Today I will talk about a novel technique called DRAIN, which provides deadlock freedom in any network topology by periodically moving packets in the network.

## Slide 104: Putting it all together
ITG generates irregular topology as per spec.
RTG creates deadlock-free routing table for irregular Topology
Files generated by ITG and RTG are integrated into DRAGON gem5
DRAGON-gem5 simulates the irr. topology
  Deadlock-prone
  Deadlock-free (using RTG)
It counts number, shape and size of deadlocks formed at runtime

## Slide 105: DRAGON: Walk through
4x4 Mesh Topology
Node-0_0:
Router-0; Inport-0
DRAGON snapshot frequency specified by gem5 command-line
5
4
5
3
6
1
3
5
Packet with Destination Router-5
Node-3_1:
Router-3; Inport-1
DRAGON takes the snapshot of current network state and create graph
Free Node
Blocked Node

## Slide 106: DRAGON: First Pass
1_1
2_0
5_2
6_3
8_1
10_1
14_1
5
4
5
3
6
1
3
DRAGON first create a graph with blocked nodes only
Routing Algorithm determines the connection between nodes
Blocked Nodes

## Slide 107: DRAGON: Second Pass (DRAGON Graph)
Any blocked node which depends on unblocked node is marked as unblocked recursively in First Pass Graph
At the end of this elimination process only blocked nodes will be present
Number of cycles in the blocked nodes will give us number of routing deadlocks
1_1
2_0
5_2
6_3
1 deadlock cycle 

## Slide 108: DRAGON Graph
Generic DRAGON Graph to analyze shape, size and number of deadlocks in any network topology

## Slide 109: Irregular Topology Generator
Irregular Topology Generator (ITG) automates the generation of irregular topology
Number of faults can be user specified
Number of random topologies can be used specified
Directly integrated to gem5
DRAGON tool + ITG can be used to study:
  Number of deadlocks for real applications
  Deadlocks Sensitivity in irregular topology for real applications

## Slide 110: ITG: Walk though
12
13
14
15
8
9
10
11
4
5
6
7
0
1
2
3
Number of Irregular Topology:
Size of topology:
Number of links removed:
Currently ITG assumes baseline Mesh topology as the starting point.
This can be modified in the code.
16
2
2
4
4
Notes: Topology is nothing but number of nodes connected in a certain fashion… here we have 16 nodes connected in a way to form ‘Mesh’ topology: Particularly 4x4 Mesh topology
-- Now I will show with the help of animations how ITG tool works
User required to provide these three parameters: ‘size of topology’, ‘number of faults’ and

## Slide 111
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
root
sender
receiver
dn
dn
dn
dn
RTG: Walk though
Schroeder, Michael D., et al. “Autonet: a high-speed, self-configuring local area network using point-to-point links” IEEE Journal on Selected Areas in Communications, 1991.
Aisopos, Konstantinos, et al. "Ariadne: Agnostic reconfiguration in a disconnected network environment" 2011 PACT. IEEE, 2011.

## Slide 112
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
root
sender
receiver
dn
up
DN->UP not allowed by routing algorithm
RTG: Walk though
Notes: Non-minimal paths in certain cases

## Slide 113
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
dn
up
DN->UP not allowed by routing algorithm
up
up
dn
dn
RTG: Walk though
root
sender
receiver

## Slide 114: Deadlock Probability: Topology Sweep
Chart: 4x4 Mesh
| Bit Complement | Bit Reverse | Bit Rotation | Shuffle | Transpose | Uniform Random
VC-1 | 0.02 | 0.08 | 0.02 | 0.06 | 100 | 0.04
VC-2 | 0.08 | 0.8 | 0.3 | 100 | 100 | 0.24
VC-4 | 0.18 | 100 | 0.68 | 100 | 100 | 0.58
Chart: 8x8 Mesh
| Bit Complement | Bit Reverse | Bit Rotation | Shuffle | Transpose | Uniform Random
VC-1 | 0.02 | 0.04 | 0.04 | 0.02 | 100 | 0.02
VC-2 | 0.04 | 0.1 | 0.14 | 0.1 | 100 | 0.1
VC-4 | 0.08 | 0.2 | 0.28 | 0.2 | 100 | 0.22
Chart: 16x16 Mesh
| Bit Complement | Bit Reverse | Bit Rotation | Shuffle | Transpose | Uniform Random
VC-1 | 0.02 | 0.02 | 0.02 | 0.02 | 100 | 0.02
VC-2 | 0.02 | 0.04 | 0.06 | 0.04 | 100 | 0.04
VC-4 | 0.04 | 0.08 | 0.14 | 0.08 | 100 | 0.1

## Slide 115: Deadlock Probability: Traffic Pattern Sweep
Chart: Bit Complement
| 4x4 Mesh | 8x8 Mesh | 16x16 Mesh
VC-1 | 0.02 | 0.02 | 0.02
VC-2 | 0.08 | 0.04 | 0.02
VC-4 | 0.18 | 0.08 | 0.04
Chart: Bit Rotation
| 4x4 Mesh | 8x8 Mesh | 16x16 Mesh
VC-1 | 0.02 | 0.04 | 0.02
VC-2 | 0.3 | 0.14 | 0.06
VC-4 | 0.68 | 0.28 | 0.14
Chart: Uniform Random
| 4x4 Mesh | 8x8 Mesh | 16x16 Mesh
VC-1 | 0.04 | 0.02 | 0.02
VC-2 | 0.24 | 0.1 | 0.04
VC-4 | 0.58 | 0.22 | 0.1

## Slide 116: Synthetic Traffic: Throughput
Chart: Uniform Random 64 nodes VC-2
| Fault-0 | Fault-1 | Fault-4 | Fault-8 | Fault-12
escapeVC | 0.1 | 0.088 | 0.077143 | 0.068 | 0.062
SPIN-1024 | 0.16 | 0.154 | 0.13 | 0.112 | 0.094667
Drain-32768 | 0.16 | 0.14889 | 0.12889 | 0.11 | 0.095714
Drain-65536 | 0.16 | 0.14889 | 0.12889 | 0.11 | 0.095714
Chart: Transpose 64 nodes VC-2
| Fault-0 | Fault-1 | Fault-4 | Fault-8 | Fault-12
escapeVC | 0.08 | 0.08 | 0.08 | 0.06 | 0.06
SPIN-1024 | 0.18 | 0.172 | 0.15 | 0.126 | 0.10667
Drain-32768 | 0.18 | 0.16889 | 0.14667 | 0.125 | 0.10143
Drain-65536 | 0.18 | 0.16667 | 0.144 | 0.125 | 0.10143

## Slide 117: Full System Results
Done on 4x4 Mesh, using Parsec3.0 with full-system
FFT shows maximum DMC
Drastic decrease in DMC with increase in VCs/input port

## Slide 118: Outline
Introduction
Prior Work in Deadlock Freedom
  Proactive
  Reactive
Contribution: Subactive Technique
  BBR
  BINDU
  DRAIN
  SWAP
  SEEC
DRAGON Tool
Conclusion and Future Work

## Slide 119: Conclusion
The Subactive Techniques

## Slide 120: Conclusion: The Subactive techniques
Deadlock is a condition which every network needs to solve
Deadlock occurs at various levels
  Routing Deadlocks
  Protocol Deadlocks
Current solutions either provide extra buffers, or restrict turns, or require expensive detection circuitry
Subactive techniques provide a unified approach to resolve routing and protocol level deadlocks:
  Do not require extra buffers
  Do not restrict turns
  Do not require deadlock detection

## Slide 121: Future Work

## Slide 122
Mayank Parasar, Natalie Enright Jerger, Paul V. Gratz, Joshua San Miguel and Tushar Krishna
Quality of Service using SWAP
mparasar3@gatech.edu
Notes: Good morning!
I am Mayank Parasar from Georgia Tech. Today I will talk about a novel technique called DRAIN, which provides deadlock freedom in any network topology by periodically moving packets in the network.

## Slide 123: Future Work: Quality of Service in Network
‘Swap’ also provide hard- guarantees for Quality of Service.
Create levels of priority among packets in the network
Only high priority packet can swap a low priority packet

## Slide 124: Quality of Service in Network : Walk-through
High priority packet can SWAP low priority packet but not vice-versa
High Priority Packet (HPP)
Path to destination
Low Priority Packet (LPP)
Destination of HPP
swap
swap
swap
Cycle
1
2
3
4
5
6

## Slide 125: Thank you!