## Slide 1: Lightweight Emulation of Virtual Channels using Swaps
Mayank Parasar and Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
synergy.ece.gatech.edu
mparasar3@gatech.edu
NocArc 2017

## Slide 2: Motivation: Buffer Management
Control
Xbar
Router
Buffers are key component in any NoC router
Manage contention
Avoid deadlocks
West
East
South
North
Core
Buffers
Source: Intel Teraflops, IEEE Micro 2007
Notes: Talk:
This is an overview image and it shows
How the cores are connected to each other in the modern CMPs
Using Mesh topology. Each node (core)here is connected to router
Which in turn is connected to other neighbouring nodes and core itself
Coming to the motivation of the talk ‘why should we need buffers at all in the topology’
It is mainly because of the following reasons:
1. Simultaneous request for the same output port can’t leave.. They need to be sequentialized therefore the other request need to be stored somewhere within the router
2. There could be difference of rated (sporadic-ness within network) of rate at which requests are producing to the rate at which it is getting consumed
3. <ask Tushar for other reasons>
The problem of buffer management gets exaggerated by having buffers at many logical level..
As explained in this slide…
buffers needed at ‘virtual network’ level
Virtual Network => Request; Response
Why do we need buffers at all…
They are required for managing multiple request over shared link..

## Slide 3: Flow Control
Flow Control options
Packet-based Flow Control
  E.g., Store and Forward, Virtual Cut-Through
Message-based Flow Control
  E.g., Circuit Switching
Flit-based Flow Control
  E.g., Wormhole, Virtual Channel
Most popular for on-chip networks

## Slide 4: Wormhole Flow Control Example
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until red proceeds
Dest for Red
Dest for Blue
6 flit buffers/input port
“Head-of-Line Blocking”

## Slide 5: Wormhole Flow Control
Pros
  More efficient buffer utilization (good for on-chip)
  Low latency
Cons
  Poor link utilization: if head flit becomes blocked, all links spanning length of packet are idle
  Cannot be re-allocated to different packet
  Suffers from head of line (HOL) blocking

## Slide 6: Virtual Channel Flow Control Example
Buffer full: blue cannot proceed
Blocked by other packets
Dest for Red
Dest for Blue
6 flit buffers/input port
3 flit buffers/VC

## Slide 7: Deep VC - Shallow VC
Buffers
Control
Xbar
Router
Buffers
Buffers
Control
Xbar
Router
Buffers
Deep Virtual Channels
Shallow Virtual Channels
Equal buffers
S
E
W
N
Are Virtual Channels always better?

## Slide 8: Motivation: Pros and Cons

## Slide 9: Pros and Cons
 |  | Wormhole | Shallow VC | Intermediate VC | Deep VC
 | Area |  |  |  | 
 | Power |  |  |  | 
Single flit Packet | Latency |  |  |  | 
 | Throughput |  |  |  | 
Multi flit Packet | Latency |  |  |  | 
 | Throughput |  |  |  | 

## Slide 10: Big Question
Can we have performance of VCs at the cost of wormhole!?
Notes: The big question

## Slide 11: Outline
Motivation
Enter SwapNoC
SwapNoC Policies
  Tail_Swap
  Credit_Swap
  Random_Swap
Comparision to VCs
Evaluation and Results
Conclusion

## Slide 12: Highlevel Idea
This Photo by Unknown Author is licensed under CC BY-NC
Virtual Channel
Wormhole
SwapNoC
Can we use same inspiration in NOC!?

## Slide 13: Swaps
Software swap vs Hardware swap
// using tmp variable
tmp = a;
a = b;
b = tmp;
// parallel assignment
a <= b;
b <= a;
a
b
b
a
tmp
clk
Software Swap
Hardware Swap

## Slide 14: MicroArc
Router
Xbar
West
East
South
North
Core
Swap
!(Swap)
Qhead
Qtail
Physical
Link
0
1
1
Analogous to circular
Shift register
clk
Swap
Decided by the policy

## Slide 15: Quick Recap

## Slide 16: Outline
Motivation
Background
Enter SwapNoC
SwapNoC Policies
  Tail_Swap
  Credit_Swap
  Random_Swap
Comparison to VCs
Evaluation and Results
Conclusion

## Slide 17: Tail_Swap
N
S
E
N
S
4
N
E
N
Router
Xbar
West
South
North
Core
East

## Slide 18: Outline
Motivation
Background
Enter SwapNoC
SwapNoC Policies
  Tail_Swap
  Credit_Swap
  Random_Swap
Comparison to VCs
Evaluation and Results
Conclusion

## Slide 19: Credit_Swap
N
S
E
N
S
N
E
N
Router
Xbar
West
South
North
Core
East
free Slots at
down stream’s
North port
free Slots at
down stream’s
South port
free Slots at
down stream’s
West port
free Slots at
local port
3
0
0
2
1

## Slide 20: Outline
Motivation
Background
Enter SwapNoC
SwapNoC Policies
  Tail_Swap
  Credit_Swap
  Random_Swap
Comparison to VCs
Evaluation and Results
Conclusion

## Slide 21: Random_Swap
Router
Xbar
West
East
South
North
Core
S
N
E
N
S
N
Random swap

## Slide 22: Outline
Motivation
Background
Enter SwapNoC
SwapNoC Policies
  Tail_Swap
  Credit_Swap
  Random_Swap
Comparision to VCs
Evaluation and Results
Conclusion

## Slide 23: Comparison to VCs
N
S
N
S
N
E
E
N
N
S
N
E
N
E
N
S
North blocked!
Frequent swaps
to emulate shallow VCs
occasional swaps
to emulate deep VCs
How to emulate shallow VCs with SwapNoC
How to emulate deep VCs with SwapNoC
SwapNoC
Shallow VCs
Deep VCs
SwapNoC

## Slide 24: Outline
Motivation
Background
Enter SwapNoC
SwapNoC Policies
  Tail_Swap
  Credit_Swap
  Random_Swap
Comparision to VCs
Evaluation and Results
Conclusion

## Slide 25: Area and Power
Chart: Number of Buffer Slots
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16
Wormhole | 13.23 | 16.646 | 19.819 | 23.094 | 26.354 | 29.535 | 32.711 | 36.014
SwapNoC | 13.578 | 16.774 | 20.087 | 23.495 | 26.729 | 30.06 | 33.288 | 36.372
VC Router | 16.385 | 24.558 | 33.254 | 41.751 | 50.464 | 59.229 | 67.923 | 76.685
Chart: Area (um2)
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16
Wormhole | 14710.9476 | 18301.5995 | 21538.8484 | 25372.8518 | 28932.8328 | 32094.83 | 35439.2304 | 39495.794
SwapNoC | 15173.3715 | 19502.0831 | 24171.6887 | 28949.2691 | 33734.8146 | 38888.0144 | 42924.7066 | 46344.4822
VC Router | 18042.5193 | 26929.6923 | 36842.0285 | 46101.0855 | 57171.1479 | 66705.2595 | 75830.4755 | 84072.7252
SwapNoC is 2x smaller in area and comsumes 2x lesser power compared to VC routers

## Slide 26: Overhead over baseline
Router
Xbar
West
East
South
North
Core
Swap
Swap
!(Swap)
Qhead
Qtail
Physical
Link
0
1
1
SwapNoC increases critical path by 8.4-9.4%
Adds 8% area and 1% power overhead over baseline wormhole routers

## Slide 27: Revisiting comparison Metric
 |  | Wormhole | Shallow VC | Intermediate VC | Deep VC | Swap-NoC
 | Area |  |  |  |  | 
 | Power |  |  |  |  | 
Single flit Packet | Latency |  |  |  |  | 
 | Throughput |  |  |  |  | 
Multi flit Packet | Latency |  |  |  |  | 
 | Throughput |  |  |  |  | 

## Slide 28: Simulation Configuration
Wormhole | Wormhole router with a N-flit deep queue
VC-Shallow | N 1-flit VCs (max number of VCs)
VC-deep | 2 N/2-flit deep and 4 N/4-flit deep VCs
SwapNoC | N-flit deep queue with Swaps
Simulation Infrastructure | 
Network-topology | 64 nodes in 8x8 Mesh
Technology node | 15nm PDK
Simulator | Garnet Network, gem5 simulator
Memory model | Ruby
Network Configuration

## Slide 29: Performance with Synthetic Traffic - I
Multi-flit Packet (5 flit = 1 packet)
SwapNoC provides 80% improvement in throughput on average

## Slide 30: Performance with Synthetic Traffic - II
SwapNoC provides about 15% improvement in throughput over wormhole and provide 40-50% more throughput over deep-VCs in edge_50 and bit_rotation
Single-flit Packet (1 flit = 1 packet)

## Slide 31: Full System simulation Result
36 % reduction in runtime over both VCs and wormhole using credit_swap and random_swap

## Slide 32: Outline
Motivation
Background
Enter SwapNoC
SwapNoC Policies
  Tail_Swap
  Credit_Swap
  Random_Swap
Comparision to VCs
Evaluation and Results
Conclusion

## Slide 33: Conclusion
Wormhole routers are area and power efficient but don’t give high performance
VCs are good for performance but comes with overhead of area and power
VC routers have more timing critical path than wormhole
SwapNoC marries the benefit of wormhole router with performance of VCs at modest area and power cost.
Thank you!
Questions